## Slide 1: Control Flow, Arrays, and Load/Store Instructions
COE 233
Logic Design and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Control Flow: Branch and Jump Instructions
Translating If Statements and Boolean Expressions
Arrays
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 3: Control Flow
High-level programming languages provide constructs:
  To make decisions in a program: IF-ELSE
  To repeat the execution of a sequence of instructions: LOOP
The ability to make decisions and repeat a sequence of instructions distinguishes a computer from a calculator
All computer architectures provide control flow instructions
Essential for making decisions and repetitions
These are the conditional branch and jump instructions

## Slide 4: MIPS Conditional Branch Instructions
MIPS compare and branch instructions:
beq Rs, Rt, label if (Rs == Rt) branch to label
bne Rs, Rt, label if (Rs != Rt) branch to label
MIPS compare to zero & branch instructions:
Compare to zero is used frequently and implemented efficiently
bltz Rs, label if (Rs < 0) branch to label
bgtz Rs, label if (Rs > 0) branch to label
blez Rs, label if (Rs <= 0) branch to label
bgez Rs, label if (Rs >= 0) branch to label
beqz and bnez are defined as pseudo-instructions.

## Slide 5: Branch Instruction Format
The branch instructions modify the PC register only
PC-Relative addressing:
If (branch is taken) PC = PC + 4 + 4×offset else PC = PC+4
Branch Instructions are of the I-type Format:
Op6
Rs5
Rt5
16-bit offset
Instruction | I-Type Format |  |  | 
beq Rs, Rt, label | Op = 4 | Rs | Rt | 16-bit Offset
bne Rs, Rt, label | Op = 5 | Rs | Rt | 16-bit Offset
blez Rs, label | Op = 6 | Rs | 0 | 16-bit Offset
bgtz Rs, label | Op = 7 | Rs | 0 | 16-bit Offset
bltz Rs, label | Op = 1 | Rs | 0 | 16-bit Offset
bgez Rs, label | Op = 1 | Rs | 1 | 16-bit Offset

## Slide 6: Unconditional Jump Instruction
The unconditional Jump instruction has the following syntax:
j label # jump to label
. . .
label:
The jump instruction is always taken
The Jump instruction is of the J-type format:
The jump instruction modifies the program counter PC:
The upper 4 bits of the PC are unchanged
Op6 = 2
26-bit address
26-bit address
00
PC4
multiple of 4

## Slide 7: Translating an IF Statement
Consider the following IF statement:
if (a == b) c = d + e; else c = d – e;
Given that a, b, c, d, e are in $t0 … $t4 respectively
How to translate the above IF statement?
bne $t0, $t1, else
addu $t2, $t3, $t4
j next
else: subu $t2, $t3, $t4
next: . . .

## Slide 8: Logical AND Expression
Programming languages use short-circuit evaluation
If first condition is false, second condition is skipped
if (($t1 > 0) && ($t2 < 0)) {$t3++;}
# One Possible Translation ...
bgtz $t1, L1 # first condition
j next # skip if false
L1: bltz $t2, L2 # second condition
j next # skip if false
L2: addiu $t3, $t3, 1 # both are true
next:

## Slide 9: Better Translation of Logical AND
Allow the program to fall through to second condition
!($t1 > 0) is equivalent to ($t1 <= 0)
!($t2 < 0) is equivalent to ($t2 >= 0)
Number of instructions is reduced from 5 to 3
if (($t1 > 0) && ($t2 < 0)) {$t3++;}
# Better Translation ...
blez $t1, next # 1st condition false?
bgez $t2, next # 2nd condition false?
addiu $t3, $t3, 1 # both are true
next:

## Slide 10: Logical OR Expression
Short-circuit evaluation for logical OR
If first condition is true, second condition is skipped
Use fall-through to keep the code as short as possible
bgtz $t1, L1 # 1st condition true?
bgez $t2, next # 2nd condition false?
L1: addiu $t3, $t3, 1 # increment $t3
next:
if (($t1 > 0) || ($t2 < 0)) {$t3++;}

## Slide 11: Compare Instructions
MIPS also provides set less than instructions
slt Rd, Rs, Rt if (Rs < Rt) Rd = 1 else Rd = 0
sltu Rd, Rs, Rt unsigned <
slti Rt, Rs, imm if (Rs < imm) Rt = 1 else Rt = 0
sltiu Rt, Rs, imm unsigned <
Signed / Unsigned comparisons compute different results
Given that: $t0 = 1 and $t1 = -1 = 0xffffffff
slt $t2, $t0, $t1 computes $t2 = 0
sltu $t2, $t0, $t1 computes $t2 = 1

## Slide 12: Compare Instruction Formats
The other comparisons are defined as pseudo-instructions:
seq, sne, sgt, sgtu, sle, sleu, sge, sgeu
Instruction | Meaning | Format |  |  |  |  | 
slt Rd, Rs, Rt | Rd=(Rs <s Rt)?1:0 | Op=0 | Rs | Rt | Rd | 0 | 0x2a
sltu Rd, Rs, Rt | Rd=(Rs <u Rt)?1:0 | Op=0 | Rs | Rt | Rd | 0 | 0x2b
slti Rt, Rs, im | Rt=(Rs <s im)?1:0 | 0xa | Rs | Rt | 16-bit immediate |  | 
sltiu Rt, Rs, im | Rt=(Rs <u im)?1:0 | 0xb | Rs | Rt | 16-bit immediate |  | 
Pseudo-Instruction | Equivalent MIPS Instructions
sgt $t2, $t0, $t1 | 
seq $t2, $t0, $t1 | 
subu $t2, $t0, $t1
sltiu $t2, $t2, 1
slt $t2, $t1, $t0

## Slide 13: Pseudo-Branch Instructions
MIPS hardware does NOT provide the following instructions:
blt, bltu branch if less than (signed / unsigned)
ble, bleu branch if less or equal (signed / unsigned)
bgt, bgtu branch if greater than (signed / unsigned)
bge, bgeu branch if greater or equal (signed / unsigned)
MIPS assembler defines them as pseudo-instructions:
Pseudo-Instruction | Equivalent MIPS Instructions
blt $t0, $t1, label | 
ble $t0, $t1, label | 
$at ($1) is the assembler temporary register
slt $at, $t0, $t1
bne $at, $zero, label
slt $at, $t1, $t0
beq $at, $zero, label

## Slide 14: Using Pseudo-Branch Instructions
Translate the IF statement to assembly language
$t1 and $t2 values are unsigned
$t3, $t4, and $t5 values are signed
  bgtu $t1, $t2, L1
  move $t3, $t4
L1:
if($t1 <= $t2) {
$t3 = $t4;
}
if (($t3 <= $t4) &&
($t4 >= $t5)) {
$t3 = $t4 + $t5;
}
  bgt $t3, $t4, L1
  blt $t4, $t5, L1
  addu $t3, $t4, $t5
L1:

## Slide 15: Conditional Move Instructions
Conditional move can eliminate branch & jump instructions
Instruction | Meaning | R-Type Format |  |  |  |  | 
movz Rd, Rs, Rt | if (Rt==0) Rd=Rs | Op=0 | Rs | Rt | Rd | 0 | 0xa
movn Rd, Rs, Rt | if (Rt!=0) Rd=Rs | Op=0 | Rs | Rt | Rd | 0 | 0xb
if ($t0 == 0) {$t1=$t2+$t3;} else {$t1=$t2-$t3;}
  bne $t0, $0, L1
  addu $t1, $t2, $t3
  j L2
  L1: subu $t1, $t2, $t3
  L2: . . .
  addu $t1, $t2, $t3
  subu $t4, $t2, $t3
  movn $t1, $t4, $t0
  . . .

## Slide 16: Next . . .
Control Flow: Branch and Jump Instructions
Translating If Statements and Boolean Expressions
Arrays
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 17: Arrays
In a high-level programming language, an array is a homogeneous data structure with the following properties:
  All array elements are of the same type and size
  Once an array is allocated, its size cannot be modified
  The base address is the address of the first array element
  The array elements can be indexed
  The address of any array element can be computed
In assembly language, an array is just a block of memory
In fact, all objects are simply blocks of memory
The memory block can be allocated statically or dynamically

## Slide 18: Static Array Allocation
An array can be allocated statically in the data segment
A data definition statement allocates static memory:
label: .type value0 [, value1 ...]
label: is the name of the array
.type directive specifies the size of each array element
value0, value1 ... specify a list of initial values
Examples of static array definitions:
arr1: .half 20, -1 # array of 2 half words
arr2: .word 1:5 # array of 5 words (value=1)
arr3: .space 20 # array of 20 bytes
str1: .asciiz "Null-terminated string"

## Slide 19: Watching Values in the Data Segment
The labels window is the symbol table
  Shows labels and corresponding addresses
The la pseudo-instruction loads the address of any label into a register

## Slide 20: Dynamic Memory Allocation
One of the functions of the OS is to manage memory
A program can allocate memory on the heap at runtime
The heap is part of the data segment that can grow at runtime
The program makes a system call ($v0=9) to allocate memory
.text
. . .
li $a0, 100 # $a0 = number of bytes to allocate
li $v0, 9 # system call 9
syscall # allocate 100 bytes on the heap
move $t0, $v0 # $t0 = address of allocated block
. . .

## Slide 21: Allocating Dynamic Memory on the Heap
Stack Segment
Heap Area
Static Area
Data Segment
0x00000000
Reserved
0x10000000
Text Segment
0x7fffffff
0x00400000
0x10040000

## Slide 22: Computing the Addresses of Elements
In a high-level programming language, an array is indexed
array[0] is the first element in the array
array[i] is the element at index i
&array[i] is the address of the element at index i
&array[i] = &array + i × element_size
For a 2D array, the array is stored linearly in memory
matrix[Rows][Cols] has (Rows × Cols) elements
&matrix[i][j] = &matrix + (i×Cols + j) × element_size
For example, to allocate a matrix[10][20] of integers:
matrix: .word 0:200 # 200 words (initialized to 0)
&matrix[1][5] = &matrix + (1×20 + 5)×4 = &matrix + 100

## Slide 23: Element Addresses in a 2D Array
&matrix[i][j] = &matrix + (i×COLS + j) × Element_size
0
1
…
i
…
ROWS-1
0
1
…
j
…
COLS-1
COLS
ROWS
Address calculation is essential when programming in assembly

## Slide 24: Load and Store Instructions
Instructions that transfer data between memory & registers
Programs include variables such as arrays and objects
These variables are stored in memory
Load Instruction:
  Transfers data from memory to a register
Store Instruction:
  Transfers data from a register to memory
Memory address must be specified by load and store
Memory
Registers
load
store

## Slide 25: Load and Store Word
Load Word Instruction (Word = 4 bytes in MIPS)
lw Rt, imm(Rs) # Rt  MEMORY[Rs+imm]
Store Word Instruction
sw Rt, imm(Rs) # Rt  MEMORY[Rs+imm]
Base / Displacement addressing is used
  Memory Address = Rs (base) + Immediate (displacement)
  Immediate16 is sign-extended to have a signed displacement
Op6
Rs5
Rt5
immediate16
Base or Displacement Addressing
Memory Word
Base address
+

## Slide 26: Example on Load & Store
Translate: A[1] = A[2] + 5 (A is an array of words)
Given that the address of array A is stored in register $t0
  lw $t1, 8($t0) # $t1 = A[2]
  addiu $t2, $t1, 5 # $t2 = A[2] + 5
  sw $t2, 4($t0) # A[1] = $t2
Index of A[2] and A[1] should be multiplied by 4. Why?
Registers
sw
lw
Memory
A[2]
A[1]
A[3]
. . .
. . .
&A + 12
&A + 8
&A + 4
&A
$t0
$t1
$t2
&A
A[2]
A[2] + 5
. . .
. . .
A[0]

## Slide 27: Load and Store Byte and Halfword
0
0
s
s
s
s
s
0
0
s
bu
b
h
hu
sign – extend
zero – extend
sign – extend
zero – extend
32-bit Register
The MIPS processor supports the following data formats:
  Byte = 8 bits, Half word = 16 bits, Word = 32 bits
Load & store instructions for bytes and half words
  lb = load byte, lbu = load byte unsigned, sb = store byte
  lh = load half, lhu = load half unsigned, sh = store halfword
Load expands a memory value to fit into a 32-bit register
Store reduces a 32-bit register value to fit in memory

## Slide 28: Load and Store Instructions
Instruction | Meaning | I-Type Format |  |  | 
lb Rt, imm(Rs) | Rt 1 MEM[Rs+imm] | 0x20 | Rs | Rt | 16-bit immediate
lh Rt, imm(Rs) | Rt 2 MEM[Rs+imm] | 0x21 | Rs | Rt | 16-bit immediate
lw Rt, imm(Rs) | Rt 4 MEM[Rs+imm] | 0x23 | Rs | Rt | 16-bit immediate
lbu Rt, imm(Rs) | Rt 1 MEM[Rs+imm] | 0x24 | Rs | Rt | 16-bit immediate
lhu Rt, imm(Rs) | Rt 2 MEM[Rs+imm] | 0x25 | Rs | Rt | 16-bit immediate
sb Rt, imm(Rs) | Rt 1 MEM[Rs+imm] | 0x28 | Rs | Rt | 16-bit immediate
sh Rt, imm(Rs) | Rt 2 MEM[Rs+imm] | 0x29 | Rs | Rt | 16-bit immediate
sw Rt, imm(Rs) | Rt 4 MEM[Rs+imm] | 0x2b | Rs | Rt | 16-bit immediate
Base / Displacement Addressing is used
  Memory Address = Rs (Base) + Immediate (displacement)
  If Rs is $zero then Address = Immediate (absolute)
  If Immediate is 0 then Address = Rs (register indirect)

## Slide 29: Next . . .
Control Flow: Branch and Jump Instructions
Translating If Statements and Boolean Expressions
Arrays
Load and Store Instructions
Translating Loops and Traversing Arrays
Addressing Modes

## Slide 30: Translating a WHILE Loop
Consider the following WHILE loop:
i = 0; while (A[i] != value && i<n) i++;
Where A is an array of integers (4 bytes per element)
Translate WHILE loop: $a0 = &A, $a1 = n, and $a2 = value
&A[i] = &A + i*4 = &A[i-1] + 4
li $t0, 0 # $t0 = i = 0
loop: lw $t1, 0($a0) # $t1 = A[i]
beq $t1, $a2, done # (A[i] == value)?
beq $t0, $a1, done # (i == n)?
addiu $t0, $t0, 1 # i++
addiu $a0, $a0, 4 # $a0 = &A[i]
j loop # jump backwards to loop
done: . . .

## Slide 31: Copying a String
loop:
lb $t0, 0($a1) # load byte: $t0 = source[i]
sb $t0, 0($a0) # store byte: target[i]= $t0
addiu $a0, $a0, 1 # $a0 = &target[i]
addiu $a1, $a1, 1 # $a1 = &source[i]
bnez $t0, loop # loop until NULL char
A string in C is an array of chars terminated with null char
i = 0;
do { ch = source[i]; target[i] = ch; i++; }
while (ch != '\0');
Given that: $a0 = &target and $a1 = &source

## Slide 32: Initializing a Column of a Matrix
M = new int[10][5]; // allocate M on the heap
int i;
for (i=0; i<10; i++) { M[i][3] = i; }
# &M[i][3] = &M + (i*5 + 3) * 4 = &M + i*20 + 12
li $a0, 200 # $a0 = 10*5*4 = 200 bytes
li $v0, 9 # system call 9
syscall # allocate 200 bytes
move $t0, $v0 # $t0 = &M
li $t1, 0 # $t1 = i = 0
li $t2, 10 # $t2 = 10
L: sw $t1, 12($t0) # store M[i][3] = i
addiu $t1, $t1, 1 # i++
addiu $t0, $t0, 20 # $t0 = &M[i][3]
bne $t1, $t2, L # if (i != 10) loop back

## Slide 33: Addressing Modes
Op6
Rs5
Rt5
16-bit immediate
Base / Displacement Addressing
Word
Memory Addressing (load/store)
Register = Base address
+
Halfword
Byte
Op6
Rs5
Rt5
16-bit immediate
Immediate Addressing
One Operand is a constant
Op6
Rs5
Rt5
Rd5
funct6
sa5
Register Addressing
Register
Operands are in registers
Where are the operands?
How memory addresses are computed?

## Slide 34: Branch / Jump Addressing Modes
Used by branch (beq, bne, …)
Word = Target Instruction
Op6
Rs5
Rt5
16-bit Offset
PC-Relative Addressing
PC30
00
+1
Branch Target Address
PC = PC + 4 × (1 + Offset)
PC30 + Offset16 + 1
00
26-bit address
PC4
00
Jump Target Address
Word = Target Instruction
26-bit address
Op6
Pseudo-direct Addressing
PC30
:
00
Used by jump instruction

## Slide 35: Jump and Branch Limits
Jump Address Boundary = 226 instructions = 256 MB
  Jump cannot reach outside its 256 MB segment boundary
  Upper 4 bits of PC are unchanged
Branch Address Boundary
  Branch instructions use I-Type format (16-bit Offset)
  PC-relative addressing:
    Branch Target address = PC + 4 × (1 + Offset)
    Count the number of instructions to skip starting at next instruction
    Positive offset  Forward branch, Negative offset  Backward branch
    Most branches are near : At most ±215 instructions can be skipped
26-bit address
PC4
00
Jump Target Address
PC30 + Offset16 + 1
00