## Slide 1: Integer Multiplication and Division
COE 233
Logic Design and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Unsigned Integer Multiplication
Paper and Pencil Example:
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
n-bit multiplicand × n-bit multiplier = (2n)-bit product
Accomplished via shifting and addition
Consumes more time and more chip area than addition
Binary multiplication is easy
0 × multiplicand = 0
1 × multiplicand = multiplicand

## Slide 3: Signed Integer Multiplication
First attempt:
  Convert multiplier and multiplicand into positive numbers
    If negative then obtain the 2's complement and remember the sign
  Perform unsigned multiplication
  Compute the sign of the product
  If product sign < 0 then obtain the 2's complement of the product
  Drawback: additional steps to compute the 2's complement
Better version:
  Use the same multiplication hardware
  Extend the sign of the multiplicand in the partial products
  If multiplier is negative, the last step should be a subtract

## Slide 4: Signed Multiplication (Paper & Pencil)
Case 1: Positive Multiplier
Multiplicand 11002 = -4
Multiplier × 01012 = +5
11111100
111100
Product 111011002 = -20
Case 2: Negative Multiplier
Multiplicand 11002 = -4
Multiplier × 11012 = -3
11111100
111100
00100 (2's complement of 1100)
Product 000011002 = +12
Sign-extension
Sign-extension

## Slide 5: Unsigned Division (Paper & Pencil)
= 19 Quotient
Divisor 10112 110110012 = 217 Dividend
-1011
10
101
1010
10100
-1011
1001
10011
-1011
10002 = 8 Remainder
Dividend =
Quotient × Divisor
+ Remainder
217 = 19 × 11 + 8
1
0
0
1
12
Check how big a number can be subtracted, creating a bit of the quotient on each attempt
Binary division is done via shifting and subtraction

## Slide 6: Signed Integer Division
Simplest way is to remember the signs
Convert the dividend and divisor to positive
  Obtain the 2's complement if they are negative
Do the unsigned division
Compute the signs of the quotient and remainder
  Quotient sign = Dividend sign XOR Divisor sign
  Remainder sign = Dividend sign
Negate the quotient and remainder if their sign is negative
  Obtain the 2's complement to convert them to negative

## Slide 7: Signed Integer Division Examples
Positive Dividend and Positive Divisor
  Example: +17 / +3 Quotient = +5 Remainder = +2
Positive Dividend and Negative Divisor
  Example: +17 / –3 Quotient = –5 Remainder = +2
Negative Dividend and Positive Divisor
  Example: –17 / +3 Quotient = –5 Remainder = –2
Negative Dividend and Negative Divisor
  Example: –17 / –3 Quotient = +5 Remainder = –2
The following equation must always hold:
Dividend = Quotient × Divisor + Remainder

## Slide 8: Integer Multiplication in MIPS
Multiply instructions
  mult Rs, Rt Signed multiplication
  multu Rs, Rt Unsigned multiplication
32-bit multiplication produces a 64-bit Product
Separate pair of 32-bit registers
  HI = high-order 32-bit of product
  LO = low-order 32-bit of product
MIPS also has a special mul instruction
  mul Rd, Rs, Rt Rd = Rs × Rt
  Copy LO into destination register Rd
  Useful when the product is small (32 bits) and HI is not needed
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 9: Integer Division in MIPS
Divide instructions
  div Rs, Rt Signed division
  divu Rs, Rt Unsigned division
Division produces quotient and remainder
Separate pair of 32-bit registers
  HI = 32-bit remainder
  LO = 32-bit quotient
  If divisor is 0 then result is unpredictable
Moving data from HI, LO to MIPS registers
  mfhi Rd (Rd = HI)
  mflo Rd (Rd = LO)
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 10: Integer Multiply and Divide Instructions
Instruction | Meaning | Format |  |  |  |  | 
mult Rs, Rt | HI, LO = Rs ×s Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x18
multu Rs, Rt | HI, LO = Rs ×u Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x19
mul Rd, Rs, Rt | Rd = Rs ×s Rt | 0x1c | Rs | Rt | Rd | 0 | 2
div Rs, Rt | HI, LO = Rs /s Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x1a
divu Rs, Rt | HI, LO = Rs /u Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x1b
mfhi Rd | Rd = HI | Op = 0 | 0 | 0 | Rd | 0 | 0x10
mflo Rd | Rd = LO | Op = 0 | 0 | 0 | Rd | 0 | 0x12
mthi Rs | HI = Rs | Op = 0 | Rs | 0 | 0 | 0 | 0x11
mtlo Rs | LO = Rs | Op = 0 | Rs | 0 | 0 | 0 | 0x13
×s = Signed multiplication, ×u = Unsigned multiplication
/s = Signed division, /u = Unsigned division
NO arithmetic exception can occur

## Slide 11: String to Integer Conversion
Consider the conversion of string "91052" into an integer
How to convert the string into an integer?
Initialize: sum = 0
Load each character of the string into a register
  Check if the character is in the range: '0' to '9'
  Convert the character into a digit in the range: 0 to 9
  Compute: sum = sum * 10 + digit
  Repeat until end of string or a non-digit character is encountered
To convert "91052", initialize sum to 0 then …
  sum = 9, then 91, then 910, then 9105, then 91052
'9'
'1'
'0'
'5'
'2'

## Slide 12: String to Integer Conversion Function
#-----------------------------------------------------------
# str2int: Convert a string of digits into unsigned integer
# Input: $a0 = address of null terminated string
# Output: $v0 = unsigned integer value
#-----------------------------------------------------------
str2int:
li $v0, 0 # Initialize: $v0 = sum = 0
li $t0, 10 # Initialize: $t0 = 10
L1: lb $t1, 0($a0) # load $t1 = str[i]
blt $t1, '0', done # exit loop if ($t1 < '0')
bgt $t1, '9', done # exit loop if ($t1 > '9')
addiu $t1, $t1, -48 # Convert character to digit
mul $v0, $v0, $t0 # $v0 = sum * 10
addu $v0, $v0, $t1 # $v0 = sum * 10 + digit
addiu $a0, $a0, 1 # $a0 = address of next char
j L1 # loop back
done: jr $ra # return to caller

## Slide 13: Integer to String Conversion
Convert an unsigned 32-bit integer into a string
How to obtain the decimal digits of the number?
  Divide the number by 10, Remainder = decimal digit (0 to 9)
  Convert decimal digit into its ASCII representation ('0' to '9')
  Repeat the division until the quotient becomes zero
  Digits are computed backwards from least to most significant
Example: convert 2037 to a string
  Divide 2037/10 quotient = 203 remainder = 7 char = '7'
  Divide 203/10 quotient = 20 remainder = 3 char = '3'
  Divide 20/10 quotient = 2 remainder = 0 char = '0'
  Divide 2/10 quotient = 0 remainder = 2 char = '2'

## Slide 14: Integer to String Conversion Function
#----------------------------------------------------------
# int2str: Converts an unsigned integer into a string
# Input: $a0 = value, $a1 = buffer address (12 bytes)
# Output: $v0 = address of converted string in buffer
#----------------------------------------------------------
int2str:
li $t0, 10 # $t0 = divisor = 10
addiu $v0, $a1, 11 # start at end of buffer
sb $zero, 0($v0) # store a NULL character
L2: divu $a0, $t0 # LO = value/10, HI = value%10
mflo $a0 # $a0 = value/10
mfhi $t1 # $t1 = value%10
addiu $t1, $t1, 48 # convert digit into ASCII
addiu $v0, $v0, -1 # point to previous byte
sb $t1, 0($v0) # store character in memory
bnez $a0, L2 # loop if value is not 0
jr $ra # return to caller