## Slide 1: MIPS Functions and the Runtime Stack
COE 233
Logic Design and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Functions
Function Call and Return
The Stack Segment
Preserving Registers
Examples: Bubble Sort and Recursion

## Slide 3: Functions
A function (or a procedure) is a block of instructions that can be called at several different points in the program
  Allows the programmer to focus on just one task at a time
  Allows code to be reused
The function that initiates the call is known as the caller
The function that receives the call is known as the callee
When the callee finishes execution, control is transferred back to the caller function.
A function can receive parameters and return results
The function parameters and results act as an interface between a function and the rest of the program

## Slide 4: Function Call and Return
To execution a function, the caller does the following:
  Puts the parameters in a place that can be accessed by the callee
  Transfer control to the callee function
To return from a function, the callee does the following:
  Puts the results in a place that can be accessed by the caller
  Return control to the caller, next to where the function call was made
Registers are the fastest place to pass parameters and return results. The MIPS architecture uses the following:
  $a0-$a3: four argument registers in which to pass parameters
  $v0-$v1: two value registers in which to pass function results
  $ra: return address register to return back to the caller

## Slide 5: Function Call and Return Instructions
JAL (Jump-and-Link) is used to call a function
  Save return address in $31 = PC+4 and jump to function
  Register $31 ($ra) is used by JAL as the return address
JR (Jump Register) is used to return from a function
  Jump to instruction whose address is in register Rs (PC = Rs)
JALR (Jump-and-Link Register)
  Save return address in Rd = PC+4, and
  Call function whose address is in register Rs (PC = Rs)
  Used to call functions whose addresses are known at runtime
Instruction | Meaning | Format |  |  |  |  | 
jal label | $31 = PC+4, j Label | Op=3 | 26-bit address |  |  |  | 
jr Rs | PC = Rs | Op=0 | Rs | 0 | 0 | 0 | 8
jalr Rd, Rs | Rd = PC+4, PC = Rs | Op=0 | Rs | 0 | Rd | 0 | 9

## Slide 6: Example
Parameters:
$a0 = Address of v[]
$a1 = k, and
Return address is in $ra
Consider the following swap function (written in C)
Translate this function to MIPS assembly language
void swap(int v[], int k)
{ int temp;
temp = v[k]
v[k] = v[k+1];
v[k+1] = temp;
}
swap:
sll $t0,$a1,2 # $t0=k*4
add $t0,$t0,$a0 # $t0=v+k*4
lw $t1,0($t0) # $t1=v[k]
lw $t2,4($t0) # $t2=v[k+1]
sw $t2,0($t0) # v[k]=$t2
sw $t1,4($t0) # v[k+1]=$t1
jr $ra # return

## Slide 7: Call / Return Sequence
Suppose we call function swap as: swap(a,10)
  Pass address of array a and 10 as arguments
  Call the function swap saving return address in $31 = $ra
  Execute function swap
  Return control to the point of origin (return address)
swap:
sll $t0,$a1,2
add $t0,$t0,$a0
lw $t1,0($t0)
lw $t2,4($t0)
sw $t2,0($t0)
sw $t1,4($t0)
jr $ra
la $a0, a
li $a1, 10
jal swap
# return here
. . .
Caller
addr a
$a0=$4
10
$a1=$5
ret addr
$ra=$31
. . .
. . .
Registers

## Slide 8: Details of JAL and JR
Register $31
is the return address register
Address Instructions Assembly Language
00400020 lui $1, 0x1001 la $a0, a
00400024 ori $4, $1, 0
00400028 ori $5, $0, 10 ori $a1,$0,10
0040002C jal 0x10000f jal swap
00400030 . . . # return here
swap:
0040003C sll $8, $5, 2 sll $t0, $a1, 2
00400040 add $8, $8, $4 add $t0, $t0, $a0
00400044 lw $9, 0($8) lw $t1, 0($t0)
00400048 lw $10,4($8) lw $t2, 4($t0)
0040004C sw $10,0($8) sw $t2, 0($t0)
00400050 sw $9, 4($8) sw $t1, 4($t0)
00400054 jr $31 jr $ra
Pseudo-Direct
Addressing
PC = imm26<<2
0x10000f << 2
= 0x0040003C
0x00400030
$31

## Slide 9: Second Example
Function tolower converts a capital letter to lowercase
If parameter ch is not a capital letter then return ch
char tolower(char ch) {
if (ch>='A' && ch<='Z')
return (ch + 'a' - 'A');
else
return ch;
}
tolower: # $a0 = parameter ch
blt $a0, 'A', else # branch if $a0 < 'A'
bgt $a0, 'Z', else # branch if $a0 > 'Z'
addi $v0, $a0, 32 # 'a' – 'A' == 32
jr $ra # return to caller
else:
move $v0, $a0 # $v0 = ch
jr $ra # return to caller

## Slide 10: Next . . .
Functions
Function Call and Return
The Stack Segment
Preserving Registers
Examples: Bubble Sort and Recursion

## Slide 11: The Stack Segment
Every program has 3 segments when loaded into memory:
  Text segment: stores machine instructions
  Data segment: area used for static and dynamic variables
  Stack segment: area that can be allocated and freed by functions
The program uses only logical (virtual) addresses
The actual (physical) addresses are managed by the OS
Stack Segment
Heap Area
Static Area
0x00000000
Reserved
0x10000000
Text Segment
0x7fffffff
0x00400000
0x10040000
Stack Grows
Downwards

## Slide 12: The Stack Segment (cont'd)
The stack segment is used by functions for:
  Passing parameters that cannot fit in registers
  Allocating space for local variables
  Saving registers across function calls
  Implement recursive functions
The stack segment is implemented via software:
  The Stack Pointer $sp = $29 (points to the top of stack)
  The Frame Pointer $fp = $30 (points to a stack frame)
The stack pointer $sp is initialized to the base address of the stack segment, just before a program starts execution
The MARS tool initializes register $sp to 0x7fffeffc

## Slide 13: Stack Frame
Stack frame is an area of the stack containing …
  Saved arguments, registers, local arrays and variables (if any)
Called also the activation frame
Frames are pushed and popped by adjusting …
  Stack pointer $sp = $29 (and sometimes frame pointer $fp = $30)
  Decrement $sp to allocate stack frame, and increment to free
Frame f()
Stack
↓
stack grows downwards
$fp
$sp
Frame f()
Stack
allocate stack frame
Frame g()
$fp
$sp
f calls g
g returns
Frame f()
Stack
↑
free stack frame
$fp
$sp
Args for nested calls
Saved registers
Local
stack
variables
$sp

## Slide 14: Leaf Function
A leaf function does its work without calling any function
Example of leaf functions are: swap and tolower
A leaf function can freely modify some registers:
  Argument registers: $a0 - $a3
  Result registers: $v0 - $v1
  Temporary registers: $t0 - $t9
  These registers can be modified without saving their old values
A leaf function does not need a stack frame if …
  Its variables can fit in temporary registers
A leaf function allocates a stack frame only if …
  It requires additional space for its local variables

## Slide 15: Non-Leaf Function
A non-leaf function is a function that calls other functions
A non-leaf function must allocate a stack frame
Stack frame size is computed by the programmer (compiler)
To allocate a stack frame of N bytes …
  Decrement $sp by N bytes: $sp = $sp – N
  N must be multiple of 4 bytes to have registers aligned in memory
  In our examples, only register $sp will be used ($fp is not needed)
Must save register $ra before making a function call
  Must save $s0-$s7 if their values are going to be modified
  Other registers can also be preserved (if needed)
  Additional space for local variables can be allocated (if needed)

## Slide 16: Steps for Function Call and Return
To make a function call …
  Make sure that register $ra is saved before making a function call
  Pass arguments in registers $a0 thru $a3
  Pass additional arguments on the stack (if needed)
  Use the JAL instruction to make a function call (JAL modifies $ra)
To return from a function …
  Place the function results in $v0 and $v1 (if any)
  Restore all registers that were saved upon function entry
    Load the register values that were saved on the stack (if any)
  Free the stack frame: $sp = $sp + N (stack frame = N bytes)
  Jump to the return address: jr $ra (return to caller)

## Slide 17: Preserving Registers
The MIPS software specifies which registers must be preserved across a function call, and which ones are not
Must be Preserved | Not preserved
Return address: $ra | Argument registers: $a0 to $a3
Stack pointer: $sp | Value registers: $v0 and $v1
Saved registers: $s0 to $s7 and $fp | Temporary registers: $t0 to $t9
Stack above the stack pointer | Stack below the stack pointer
Caller saves register $ra before making a function call
A callee function must preserve $sp, $s0 to $s7, and $fp.
If needed, the caller can save argument registers $a0 to $a3. However, the callee function is free to modify them.

## Slide 18: Example on Preserving Register
A function f calls g twice as shown below. We don't know what g does, or which registers are used in g.
We only know that function g receives two integer arguments and returns one integer result. Translate f:
int f(int a, int b) {
int d = g(b, g(a, b));
return a + d;
}

## Slide 19: Translating Function f
int f(int a, int b) {
int d = g(b, g(a, b)); return a + d;
}
f: addiu $sp, $sp, -12 # allocate frame = 12 bytes
sw $ra, 0($sp) # save $ra
sw $a0, 4($sp) # save a (caller-saved)
sw $a1, 8($sp) # save b (caller-saved)
jal g # call g(a,b)
lw $a0, 8($sp) # $a0 = b
move $a1, $v0 # $a1 = result of g(a,b)
jal g # call g(b, g(a,b))
lw $a0, 4($sp) # $a0 = a
addu $v0, $a0, $v0 # $v0 = a + d
lw $ra, 0($sp) # restore $ra
addiu $sp, $sp, 12 # free stack frame
jr $ra # return to caller

## Slide 20: Next . . .
Functions
Function Call and Return
The Stack Segment
Preserving Registers
Examples: Bubble Sort and Recursion

## Slide 21: Bubble Sort (Leaf Function)
void bubbleSort (int A[], int n) {
int swapped, i, temp;
do {
n = n-1;
swapped = 0; // false
for (i=0; i<n; i++) {
if (A[i] > A[i+1]) {
temp = A[i]; // swap A[i]
A[i] = A[i+1]; // with A[i+1]
A[i+1] = temp;
swapped = 1; // true
}
}
} while (swapped);
}
Worst case Performance O(n2)
Best case Performance O(n)

## Slide 22: Translating Function Bubble Sort
bubbleSort: # $a0 = &A, $a1 = n
do: addiu $a1, $a1, -1 # n = n-1
blez $a1, L2 # branch if (n <= 0)
move $t0, $a0 # $t0 = &A
li $t1, 0 # $t1 = swapped = 0
li $t2, 0 # $t2 = i = 0
for: lw $t3, 0($t0) # $t3 = A[i]
lw $t4, 4($t0) # $t4 = A[i+1]
ble $t3, $t4, L1 # branch if (A[i] <= A[i+1])
sw $t4, 0($t0) # A[i] = $t4
sw $t3, 4($t0) # A[i+1] = $t3
li $t1, 1 # swapped = 1
L1: addiu $t2, $t2, 1 # i++
addiu $t0, $t0, 4 # $t0 = &A[i]
bne $t2, $a1, for # branch if (i != n)
bnez $t1, do # branch if (swapped)
L2: jr $ra # return to caller

## Slide 23: Example of a Recursive Function
Two recursive calls
  First call computes the sum of the first half of the array elements
  Second call computes the sum of the 2nd half of the array elements
How to translate a recursive function into assembly?
int recursive_sum (int A[], int n) {
if (n == 0) return 0;
if (n == 1) return A[0];
int sum1 = recursive_sum (&A[0], n/2);
int sum2 = recursive_sum (&A[n/2], n – n/2);
return sum1 + sum2;
}

## Slide 24: Illustrating Recursive Calls
recursive_sum:
$a0 = &A[0], $a1 = 6
recursive_sum:
$a0 = &A[0]
$a1 = 1
recursive_sum:
$a0 = &A[1]
$a1 = 2
A[1]+A[2]
A[0]
recursive_sum:
$a0 = &A[3]
$a1 = 1
recursive_sum:
$a0 = &A[4]
$a1 = 2
A[4]+A[5]
A[3]
recursive_sum:
$a0 = &A[4]
$a1 = 1
recursive_sum:
$a0 = &A[5]
$a1 = 1
A[5]
A[4]
recursive_sum:
$a0 = &A[1]
$a1 = 1
recursive_sum:
$a0 = &A[2]
$a1 = 1
A[2]
A[1]
recursive_sum:
$a0 = &A[0], $a1 = 3
recursive_sum:
$a0 = &A[3], $a1 = 3
A[3]+A[4]+A[5]
A[0]+A[1]+A[2]
$v0 = A[0]+A[1]+A[2]+A[3]+A[4]+A[5]

## Slide 25: Translating a Recursive Function
recursive_sum: # $a0 = &A, $a1 = n
bnez $a1, L1 # branch if (n != 0)
li $v0, 0
jr $ra # return 0
L1: bne $a1, 1, L2 # branch if (n != 1)
lw $v0, 0($a0) # $v0 = A[0]
jr $ra # return A[0]
L2: addiu $sp, $sp, -12 # allocate frame = 12 bytes
sw $ra, 0($sp) # save $ra
sw $s0, 4($sp) # save $s0
sw $s1, 8($sp) # save $s1
move $s0, $a0 # $s0 = &A (preserved)
move $s1, $a1 # $s1 = n (preserved)
srl $a1, $a1, 1 # $a1 = n/2
jal recursive_sum # first recursive call

## Slide 26: Translating a Recursive Function (cont'd)
$ra, $s0, and $s1 are preserved across recursive calls
srl $t0, $s1, 1 # $t0 = n/2
sll $t1, $t0, 2 # $t1 = (n/2) * 4
addu $a0, $s0, $t1 # $a0 = &A[n/2]
subu $a1, $s1, $t0 # $a1 = n – n/2
move $s0, $v0 # $s0 = sum1 (preserved)
jal recursive_sum # second recursive call
addu $v0, $s0, $v0 # $v0 = sum1 + sum2
lw $ra, 0($sp) # restore $ra
lw $s0, 4($sp) # restore $s0
lw $s1, 8($sp) # restore $s1
addiu $sp, $sp, 12 # free stack frame
jr $ra # return to caller