## Slide 1: CPU Performance
COE 233
Logic Design and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Response Time and Throughput
CPU Performance Equation
Single-Cycle versus Multi-Cycle CPU Performance
MIPS Performance Metric
Amdahl’s Law

## Slide 3: Response Time and Throughput
Response Time
  Time between start and completion of a task, as observed by end user
  Response Time = CPU Time + Waiting Time (I/O, OS scheduling, etc.)
Throughput
  Number of tasks the machine can run in a given period of time
Decreasing execution time improves throughput
  Example: using a faster version of a processor
  Less time to run a task  more tasks can be executed
Increasing throughput can also improve response time
  Example: increasing number of processors in a multiprocessor
  More tasks can be executed in parallel
  Execution time of individual sequential tasks is not changed
  But less waiting time in scheduling queue reduces response time
Notes: Have them raise their hands when answering questions

## Slide 4: Higher Performance = Less Execution Time
For some program running on machine X
X is n times faster than Y
Execution timeX
1
PerformanceX =
PerformanceY
PerformanceX
Execution timeX
Execution timeY
= n
=

## Slide 5: What do we mean by Execution Time?
Real Elapsed Time
  Counts everything:
    Waiting time, Input/output, disk access, OS scheduling, … etc.
  Useful number, but often not good for comparison purposes
Our Focus: CPU Execution Time
  Time spent while executing the program instructions
  Doesn't count the waiting time for I/O or OS scheduling
  Can be measured in seconds, or
  Can be related to number of CPU clock cycles
CPU Execution Time = CPU cycles × Cycle time
Clock rate
CPU cycles
=

## Slide 6: What is the Clock Cycle?
Clock Cycle = Clock period
  Duration between two consecutive rising edges of the clock signal
Clock rate = Clock frequency = 1 / Clock Cycle
  1 Hz = 1 cycle/sec 1 KHz = 103 cycles/sec
  1 MHz = 106 cycles/sec 1 GHz = 109 cycles/sec
  2 GHz clock has a cycle time = 1/(2×109) = 0.5 nanosecond (ns)
Clock
Data transfer & Computation
Update state
Clock Cycle
Clock Cycle 1
Clock Cycle 2
Clock Cycle 3
Operation of digital hardware is governed by a clock

## Slide 7: Improving Performance
To improve performance, we need to
  Reduce the number of clock cycles required by a program, or
  Reduce the clock cycle time (increase the clock rate)
Example:
  A program runs in 10 seconds on computer X with 2 GHz clock
  What is the number of CPU cycles on computer X ?
  We want to design computer Y to run same program in 6 seconds
  But computer Y requires 10% more cycles to execute program
  What is the clock rate for computer Y ?
Solution:
  CPU cycles on computer X = 10 sec × 2 × 109 cycles/s = 20 × 109 cycles
  CPU cycles on computer Y = 1.1 × 20 × 109 = 22 × 109 cycles
  Clock rate for computer Y = 22 × 109 cycles / 6 sec = 3.67 GHz

## Slide 8: Clock Cycles per Instruction (CPI)
Instructions take different number of cycles to execute
  Multiplication takes more time than addition
  Floating point operations take longer than integer ones
  Accessing memory takes more time than accessing registers
CPI is an average number of clock cycles per instruction
Important point
Changing the cycle time often changes the number of cycles required for various instructions
1
I1
cycles
I2
I3
I6
I4
I5
I7
2
3
4
5
6
7
8
9
10
11
12
13
14
CPI =
14/7 = 2.0

## Slide 9: Performance Equation
To execute, a given program will require …
  Some number of machine instructions
  Some number of clock cycles
  Some number of seconds
We can relate CPU clock cycles to instruction count
Performance Equation: (related to instruction count)
CPU cycles = Instruction Count × CPI
CPU Execution Time = Instruction Count × CPI × Cycle time

## Slide 10: Understanding Performance Equation
 | I-Count | CPI | Cycle
Program | X |  | 
Compiler | X | X | 
ISA | X | X | 
Organization |  | X | X
Technology |  |  | X
Execution Time = Instruction Count × CPI × Cycle time

## Slide 11: Using the Performance Equation
Suppose we have two implementations of the same ISA
For a given program
  Machine A has a clock cycle time of 250 ps and a CPI of 2.0
  Machine B has a clock cycle time of 500 ps and a CPI of 1.2
  Which machine is faster for this program, and by how much?
Solution:
  Both computer execute same count of instructions = I
  CPU execution time (A) = I × 2.0 × 250 ps = 500 × I ps
  CPU execution time (B) = I × 1.2 × 500 ps = 600 × I ps
  Computer A is faster than B by a factor = = 1.2
600 × I
500 × I

## Slide 12: Determining the CPI
Different types of instructions have different CPI
Let CPIi = clocks per instruction for class i of instructions
Let Ci = instruction count for class i of instructions
Designers often obtain CPI by a detailed simulation
Hardware counters are also used for operational CPUs
CPU cycles = (CPIi × Ci)
i = 1
n
∑
CPI =
(CPIi × Ci)
i = 1
n
∑
i = 1
n
∑
Ci

## Slide 13: Example on Determining the CPI
Problem
A compiler designer is trying to decide between two code sequences for a particular machine. Based on the hardware implementation, there are three different classes of instructions: class A, class B, and class C, and they require one, two, and three cycles per instruction, respectively.
The first code sequence has 5 instructions: 2 of A, 1 of B, and 2 of C
The second sequence has 6 instructions: 4 of A, 1 of B, and 1 of C
Compute the CPU cycles for each sequence. Which sequence is faster?
What is the CPI for each sequence?
Solution
CPU cycles (1st sequence) = (2×1) + (1×2) + (2×3) = 2+2+6 = 10 cycles
CPU cycles (2nd sequence) = (4×1) + (1×2) + (1×3) = 4+2+3 = 9 cycles
Second sequence is faster, even though it executes one extra instruction
CPI (1st sequence) = 10/5 = 2 CPI (2nd sequence) = 9/6 = 1.5

## Slide 14: Second Example on CPI
Given: instruction mix of a program on a RISC processor
What is average CPI?
What is the percent of time used by each instruction class?
Classi Freqi CPIi
ALU 50% 1
Load 20% 5
Store 10% 3
Branch 20% 2
How faster would the machine be if load time is 2 cycles?
What if two ALU instructions could be executed at once?
CPIi × Freqi
0.5×1 = 0.5
0.2×5 = 1.0
0.1×3 = 0.3
0.2×2 = 0.4
%Time
0.5/2.2 = 23%
1.0/2.2 = 45%
0.3/2.2 = 14%
0.4/2.2 = 18%
Average CPI = 0.5+1.0+0.3+0.4 = 2.2

## Slide 15: Presentation Outline
Response Time and Throughput
CPU Performance Equation
Single-Cycle versus Multi-Cycle CPU Performance
MIPS Performance Metric
Amdahl’s Law

## Slide 16: Drawback of Single Cycle Processor
Single Cycle  CPI = 1 for all instructions
Major drawback is the Long cycle time
All instructions take as much time as the slowest instruction
longest delay
Instruction
Fetch
ALU
Decode
Reg Read
ALU
Reg
Write
Load
Instruction
Fetch
Decode
Reg Read
Compute
Address
Reg
Write
Memory Read
Store
Instruction
Fetch
Decode
Reg Read
Compute
Address
Memory Write
Jump
Instruction
Fetch
Decode &
Update PC
Branch
Instruction
Fetch
Reg Read
Br Target
Compare &
Update PC

## Slide 17: Alternative: Multicycle Implementation
Break instruction execution into multiple stages
  Instruction fetch
  Instruction decode, register read, target address for jump/branch
  Execution, memory address calculation, or branch outcome
  Memory access or ALU instruction completion
  Load instruction completion
One clock cycle per stage (clock cycle is reduced)
  First 2 stages are the same for all instructions
Instruction | # cycles | Instruction | # cycles
ALU & Store | 4 | Branch | 3
Load | 5 | Jump | 2

## Slide 18: Single-Cycle versus Multi-Cycle Performance
Assume the following operation times for components:
  Access time for Instruction and data memories: 200 ps
  Delay in ALU and adders: 180 ps
  Delay in Decode and Register file access (read or write): 150 ps
  Ignore the other delays in PC, mux, extender, and wires
Which of the following would be faster and by how much?
  Single-cycle implementation for all instructions
  Multi-cycle implementation optimized for every class of instructions
    Load = 5 cycles, ALU = Store = 4 cycles, Branch = 3 cycles, Jump = 2 cycles
Assume the following instruction mix:
  40% ALU, 20% Loads, 10% stores, 20% branches, & 10% jumps

## Slide 19: Solution
Instruction Class | Instruction Memory | Register Read | ALU Operation | Data Memory | Register Write | Total
ALU | 200 | 150 | 180 |  | 150 | 680 ps
Load | 200 | 150 | 180 | 200 | 150 | 880 ps
Store | 200 | 150 | 180 | 200 |  | 730 ps
Branch | 200 | 150 | 180 |  |  | 530 ps
Jump | 200 | 150 |  |  |  | 350 ps
For fixed single-cycle implementation:
  Clock cycle =
For multi-cycle implementation:
  Clock cycle =
  Average CPI =
Speedup =
0.4×4 + 0.2×5 + 0.1×4+ 0.2×3 + 0.1×2 = 3.8
max (200, 150, 180) = 200 ps (maximum delay at any step)
880 ps determined by longest delay (load instruction)
(1 × 880 ps) / (3.8 × 200 ps) = 880 / 760 = 1.16
Compare and update PC
Decode and update PC

## Slide 20: MIPS Performance Metric
MIPS: Millions Instructions Per Second
Sometimes used as performance metric
  Faster machine  larger MIPS
MIPS specifies instruction execution rate
We can also relate execution time to MIPS
Instruction Count
Execution Time × 106
Clock Rate
CPI × 106
MIPS =
=
Inst Count
MIPS × 106
Inst Count × CPI
Clock Rate
Execution Time =
=
Notes: Book page 61 has an example to show that a machine with a bigger MIPS performance worse than a machine with a smaller MIPS

## Slide 21: Drawbacks of MIPS
Three problems using MIPS as a performance metric
Does not take into account the capability of instructions
  Cannot use MIPS to compare computers with different instruction sets because the instruction count will differ
MIPS varies between programs on the same computer
  A computer cannot have a single MIPS rating for all programs
MIPS can vary inversely with performance
  A higher MIPS rating does not always mean better performance
  Example in next slide shows this anomalous behavior

## Slide 22: MIPS example
Two different compilers are being tested on the same program for a 4 GHz machine with three different classes of instructions: Class A, Class B, and Class C, which require 1, 2, and 3 cycles, respectively.
The instruction count produced by the first compiler is 5 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
The second compiler produces 10 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
Which compiler produces a higher MIPS?
Which compiler produces a better execution time?

## Slide 23: Solution to MIPS Example
First, we find the CPU cycles for both compilers
  CPU cycles (compiler 1) = (5×1 + 1×2 + 1×3)×109 = 10×109
  CPU cycles (compiler 2) = (10×1 + 1×2 + 1×3)×109 = 15×109
Next, we find the execution time for both compilers
  Execution time (compiler 1) = 10×109 cycles / 4×109 Hz = 2.5 sec
  Execution time (compiler 2) = 15×109 cycles / 4×109 Hz = 3.75 sec
Compiler1 generates faster program (less execution time)
Now, we compute MIPS rate for both compilers
  MIPS = Instruction Count / (Execution Time × 106)
  MIPS (compiler 1) = (5+1+1) × 109 / (2.5 × 106) = 2800
  MIPS (compiler 2) = (10+1+1) × 109 / (3.75 × 106) = 3200
So, code from compiler 2 has a higher MIPS rating !!!

## Slide 24: Amdahl’s Law
Amdahl's Law is a measure of Speedup
  How a program performs after improving portion of a computer
  Relative to how it performed previously
Let f = Fraction of the computation time that is enhanced
Let s = Speedup factor of the enhancement only
Speedupoverall = =
Execution Time new
Execution Time old
((1 – f ) + f / s)
1
Fraction f of old time to be enhanced
1 – f
f / s of old time
Execution Time old
Execution Time new
1 – f

## Slide 25: Example on Amdahl's Law
Suppose a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time. How much do we have to improve the speed of multiplication if we want the program to run 4 times faster?
Solution: suppose we improve multiplication by a factor s
25 sec (4 times faster) = 80 sec / s + 20 sec
s = 80 / (25 – 20) = 80 / 5 = 16
Improve the speed of multiplication by s = 16 times
How about making the program 5 times faster?
20 sec ( 5 times faster) = 80 sec / s + 20 sec
s = 80 / (20 – 20) = ∞ Impossible to make 5 times faster!

## Slide 26: Example 2 on Amdahl's Law
Suppose that floating-point square root is responsible for 20% of the execution time of a graphics benchmark and ALL FP instructions are responsible for 60%
One proposal is to speedup FP SQRT by a factor of 10
Alternative choice: make ALL FP instructions 2X faster, which choice is better?
Answer:
  Choice 1: Improve FP SQRT by a factor of 10
  Speedup (FP SQRT) = 1/(0.8 + 0.2/10) = 1.22
  Choice 2: Improve ALL FP instructions by a factor of 2
  Speedup = 1/(0.4 + 0.6/2) = 1.43  Better