## Slide 1: Pipelined Processor Design
COE 233
Logic Design and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Serial versus Pipelined Execution
Pipelined Datapath and Control
Pipeline Hazards
Data Hazards and Forwarding
Load Delay, Hazard Detection, and Stall
Control Hazards

## Slide 3: Laundry Example
Laundry Example: Three Stages
Wash dirty load of clothes
Dry wet clothes
Fold and put clothes into drawers
Each stage takes 30 minutes to complete
Four loads of clothes to wash, dry, and fold
A
B
C
D

## Slide 4: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
Intuitively, we can use pipelining to speed up laundry
Time
6 PM
A
30
30
30
7
8
9
10
11
12 AM
30
30
30
B
30
30
30
C
30
30
30
D

## Slide 5: Pipelined Laundry: Start Load ASAP
Pipelined laundry takes 3 hours for 4 loads
Speedup factor is 2 for 4 loads
Time to wash, dry, and fold one load is still the same (90 minutes)
Time
6 PM
A
30
7
8
9 PM
B
30
30
C
30
30
30
D
30
30
30
30
30
30

## Slide 6: Serial versus Pipelined Execution
Consider a task that can be divided into k subtasks
  The k subtasks are executed on k different stages
  Each subtask requires one time unit
  The total execution time of the task is k time units
Pipelining is to overlap the execution
  The k stages work in parallel on k different tasks
  Tasks enter/leave pipeline at the rate of one task per time unit
1
2
k
…
1
2
k
…
1
2
k
…
1
2
k
…
1
2
k
…
1
2
k
…
Serial Execution
One completion every k time units
Pipelined Execution
One completion every 1 time unit

## Slide 7: Synchronous Pipeline
Uses clocked registers between stages
Upon arrival of a clock edge …
  All registers hold the results of previous stages simultaneously
The pipeline stages are combinational logic circuits
It is desirable to have balanced stages
  Approximately equal delay in all stages
Clock period is determined by the maximum stage delay
S1
S2
Sk
Register
Register
Register
Register
Input
Clock
Output

## Slide 8: Pipeline Performance
Let ti = time delay in stage Si
Clock cycle t = max(ti) is the maximum stage delay
Clock frequency f = 1/t = 1/max(ti)
A pipeline can process n tasks in k + n – 1 cycles
  k cycles are needed to complete the first task
  n – 1 cycles are needed to complete the remaining n – 1 tasks
Ideal speedup of a k-stage pipeline over serial execution
k + n – 1
Pipelined execution in cycles
Serial execution in cycles
=
=
Sk → k for large n
nk
Sk

## Slide 9: MIPS Processor Pipeline
Five stages, one cycle per stage
IF: Instruction Fetch from instruction memory
ID: Instruction Decode, register read, and J/Br address
EX: Execute operation or calculate load/store address
MEM: Memory access for load and store
WB: Write Back result to register

## Slide 10: Single-Cycle vs Pipelined Performance
Consider a 5-stage instruction execution in which …
  Instruction fetch = ALU operation = Data memory access = 200 ps
  Register read = register write = 150 ps
What is the clock cycle of the single-cycle processor?
What is the clock cycle of the pipelined processor?
What is the speedup factor of pipelined execution?
Solution
Single-Cycle Clock =
200+150+200+200+150 = 900 ps
Reg
ALU
MEM
IF
900 ps
Reg
Reg
ALU
MEM
IF
900 ps
Reg

## Slide 11: Single-Cycle versus Pipelined – cont’d
Pipelined clock cycle =
CPI for pipelined execution =
  One instruction completes each cycle (ignoring pipeline fill)
Speedup of pipelined execution =
  Instruction count and CPI are equal in both cases
Speedup factor is less than 5 (number of pipeline stage)
  Because the pipeline stages are not balanced
900 ps / 200 ps = 4.5
1
max(200, 150) = 200 ps
200
IF
Reg
MEM
ALU
Reg
IF
Reg
MEM
Reg
ALU
IF
Reg
MEM
ALU
Reg
200
200
200
200
200
200

## Slide 12: Pipeline Performance Summary
Pipelining doesn’t improve latency of a single instruction
However, it improves throughput of entire workload
  Instructions are initiated and completed at a higher rate
In a k-stage pipeline, k instructions operate in parallel
  Overlapped execution using multiple hardware resources
  Potential speedup = number of pipeline stages k
Pipeline rate is limited by slowest pipeline stage
Unbalanced lengths of pipeline stages reduces speedup
Also, time to fill and drain pipeline reduces speedup

## Slide 13: Next . . .
Serial versus Pipelined Execution
Pipelined Datapath and Control
Pipeline Hazards
Data Hazards and Forwarding
Load Delay, Hazard Detection, and Stall
Control Hazards

## Slide 14: Single-Cycle Datapath
Shown below is the single-cycle datapath
How to pipeline this single-cycle datapath?
Answer: Introduce pipeline registers at end of each stage
Branch Target Address
A
L
U
Address
Instruction
Instruction
Memory
Rs
Rd
Ext
Rt
Jump Target = PC[31:28] ‖ Imm26
ALU result
clk
PC
00
Data
Memory
Address
Data_in
Data_out
Registers
RA
RB
BusA
BusB
RW
BusW
1
0
Imm16
Next PC Address
0
1
1
0
+
0
1
2
IF = Instruction Fetch
+1
ID = Instruction Decode
& Register Read
EX = Execute
MEM = Memory Access
WB = Write Back
ALUOp
RegWr
RegDst
ALUSrc
MemRd
MemWr
WBdata
PCSrc
ExtOp
Zero

## Slide 15: Pipelined Datapath
clk
Pipeline registers are shown in green, including the PC
Same clock edge updates all pipeline registers and PC
  In addition to updating register file and data memory (for store)
Branch Target Address
A
L
U
Address
Instruction
Instruction
Memory
Rs
Rd
Ext
Rt
Jump Target = PC[31:28] ‖ Imm26
ALU Result
1
0
Imm16
Next PC Address
0
1
+
0
1
2
IF = Instruction Fetch
+1
ID = Instruction Decode
& Register Read
EX = Execute
MEM = Memory Access
WB = Write Back
ALUOp
RegWr
RegDst
ALUSrc
MemRd
MemWr
1
0
WBdata
PCSrc
ExtOp
Zero
Data
Memory
Address
Data_in
Data_out
Registers
RA
RB
BusA
BusB
RW
BusW
PC
00
Inst
NPC
BTA
A
B
Imm
D
R
Data

## Slide 16: Problem with Register Destination
Instruction in ID stage is different from the one in WB stage
  WB stage is writing to a different destination register
  Writing the destination register of the instruction in the ID Stage
1
RegDst
0
clk
Branch Target Address
A
L
U
Address
Instruction
Instruction
Memory
Rs
Rd
Ext
Rt
Jump Target = PC[31:28] ‖ Imm26
ALU Result
Data
Memory
Address
Data_in
Data_out
Registers
RA
RB
BusA
BusB
RW
BusW
1
0
Imm16
Next PC Address
+
0
1
2
IF = Instruction Fetch
+1
ID = Instruction Decode
& Register Read
EX = Execute
MEM = Memory Access
WB = Write Back
ALUOp
RegWr
ALUSrc
MemRd
MemWr
1
0
WBdata
PCSrc
ExtOp
Zero
PC
00
Inst
NPC
BTA
A
B
Imm
D
R
Data

## Slide 17: Pipelining the Destination Register
Registers
RA
RB
BusA
BusB
RW
BusW
Destination Register should be pipelined from ID to WB
  The WB stage writes back data knowing the destination register
clk
Branch Target Address
A
L
U
Address
Instruction
Instruction
Memory
Rs
Rd
Ext
Rt
Jump Target = PC[31:28] ‖ Imm26
ALU Result
Data
Memory
Address
Data_in
Data_out
1
0
Imm16
Next PC Address
RegDst
+
0
1
2
IF = Instruction Fetch
+1
ID = Instruction Decode
& Register Read
EX = Execute
MEM = Memory Access
WB = Write Back
ALUOp
RegWr
ALUSrc
MemRd
MemWr
1
0
WBdata
PCSrc
ExtOp
Zero
PC
00
Inst
NPC
BTA
A
B
Imm
D
R
Data
1
0
Rd2
Rd3
Rd4

## Slide 18: Graphically Representing Pipelines
Multiple instruction execution over multiple clock cycles
  Instructions are listed in execution order from top to bottom
  Clock cycles move from left to right
  Figure shows the use of resources at each stage and each cycle
Time (in cycles)
Program Execution Order
add $s1, $s2, $s3
CC2
Reg
IM
DM
Reg
sub $t5, $s2, $t3
CC4
ALU
IM
sw $s2, 10($t3)
DM
Reg
CC5
Reg
ALU
IM
DM
Reg
CC6
Reg
ALU
DM
CC7
Reg
ALU
CC8
Reg
DM
lw $t6, 8($s5)
IM
CC1
Reg
ori $s4, $t3, 7
ALU
CC3
IM

## Slide 19: Instruction-Time Diagram
Instruction-Time Diagram shows:
  Which instruction occupying what stage at each clock cycle
Instruction flow is pipelined over the 5 stages
IF
WB
–
EX
ID
WB
–
EX
WB
MEM
–
ID
IF
EX
ID
IF
  Time
  CC1
  CC4
  CC5
  CC6
  CC7
  CC8
  CC9
  CC2
  CC3
MEM
EX
ID
IF
WB
MEM
EX
ID
IF
lw $t7, 8($s3)
lw $t6, 8($s5)
ori $t4, $s3, 7
sub $s5, $s2, $t3
sw $s2, 10($s3)
Instruction Order
Up to five instructions can be in the pipeline during the same cycle
Instruction Level Parallelism (ILP)
ALU instructions skip the MEM stage. Store instructions skip the WB stage

## Slide 20: Control Signals
Same control signals used in the single-cycle datapath
Registers
RA
RB
BusA
BusB
RW
BusW
clk
Branch Target Address
A
L
U
Address
Instruction
Instruction
Memory
Rs
Rd
Ext
Rt
Jump Target = PC[31:28] ‖ Imm26
ALU Result
Data
Memory
Address
Data_in
Data_out
1
0
Imm16
Next PC Address
RegDst
+
0
1
2
IF = Instruction Fetch
+1
ID = Instruction Decode
EX = Execute
MEM = Memory Access
WB = Write Back
ALUOp
RegWr
ALUSrc
MemRd
MemWr
1
0
WBdata
PCSrc
ExtOp
Zero
PC
00
Inst
NPC
BTA
A
B
Imm
D
R
Data
1
0
Rd2
Rd3
Rd4

## Slide 21: Pipelined Control
RegWr
WB
MemRd
MemWr
WBdata
PCSrc
RegDst
EX
ExtOp
ExtOp
Registers
RA
RB
BusA
BusB
RW
BusW
clk
Branch Target Address
A
L
U
Address
Instruction
Instruction
Memory
Rs
Rd
Ext
Rt
Jump Target = PC[31:28] ‖ Imm26
ALU Result
Data
Memory
Address
Data_in
Data_out
1
0
Imm16
Next PC Address
+
0
1
2
IF = Instruction Fetch
+1
ID = Instruction Decode
EX = Execute
MEM = Memory Access
WB = Write Back
1
0
PC
00
Inst
NPC
BTA
A
B
Imm
D
R
Data
1
0
Rd2
Rd3
Rd4
Main & ALU
Control
Op
func
ALUSrc
ALUOp
MEM
Pipeline control signals just like data
Zero
PC
Control
Zero
J
BEQ, BNE

## Slide 22: Pipelined Control – Cont'd
ID stage generates all the control signals
Pipeline the control signals as the instruction moves
  Extend the pipeline registers to include the control signals
Each stage uses some of the control signals
  Instruction Decode and Register Read
    Control signals are generated
    RegDst and ExtOp are used in this stage, J (Jump) is used by PC control
  Execution Stage => ALUSrc, ALUOp, BEQ, BNE
    ALU generates zero signal for PC control logic (Branch Control)
  Memory Stage => MemRd, MemWr, and WBdata
  Write Back Stage => RegWr control signal is used in the last stage

## Slide 23: Control Signals Summary
Op | Decode Stage |  | Execute Stage |  | Memory Stage |  |  | Write Back | PC Control
 | RegDst | ExtOp | ALUSrc | ALUOp | MemRd | MemWr | WBdata | RegWr | PCSrc
R-Type | 1=Rd | X | 0=Reg | func | 0 | 0 | 0 | 1 | 0 = next PC
ADDI | 0=Rt | 1=sign | 1=Imm | ADD | 0 | 0 | 0 | 1 | 0 = next PC
SLTI | 0=Rt | 1=sign | 1=Imm | SLT | 0 | 0 | 0 | 1 | 0 = next PC
ANDI | 0=Rt | 0=zero | 1=Imm | AND | 0 | 0 | 0 | 1 | 0 = next PC
ORI | 0=Rt | 0=zero | 1=Imm | OR | 0 | 0 | 0 | 1 | 0 = next PC
LW | 0=Rt | 1=sign | 1=Imm | ADD | 1 | 0 | 1 | 1 | 0 = next PC
SW | X | 1=sign | 1=Imm | ADD | 0 | 1 | X | 0 | 0 = next PC
BEQ | X | X | 0=Reg | SUB | 0 | 0 | X | 0 | 0 or 2 = BTA
BNE | X | X | 0=Reg | SUB | 0 | 0 | X | 0 | 0 or 2 = BTA
J | X | X | X | X | 0 | 0 | X | 0 | 1 = jump target
PCSrc = 0 or 2 (BTA) for BEQ and BNE, depending on the zero flag

## Slide 24: Next . . .
Serial versus Pipelined Execution
Pipelined Datapath and Control
Pipeline Hazards
Data Hazards and Forwarding
Load Delay, Hazard Detection, and Stall
Control Hazards

## Slide 25: Pipeline Hazards
Hazards: situations that would cause incorrect execution
  If next instruction were launched during its designated clock cycle
Structural hazards
  Caused by resource contention
  Using same resource by two instructions during the same cycle
Data hazards
  An instruction may compute a result needed by next instruction
  Data hazards are caused by data dependencies between instructions
Control hazards
  Caused by instructions that change control flow (branches/jumps)
  Delays in changing the flow of control
Hazards complicate pipeline control and limit performance

## Slide 26: Structural Hazards
Problem
  Attempt to use the same hardware resource by two different
  instructions during the same clock cycle
Example
  Writing back ALU result in stage 4
  Conflict with writing load data in stage 5
WB
WB
EX
ID
WB
EX
MEM
IF
ID
IF
  Time
  CC1
  CC4
  CC5
  CC6
  CC7
  CC8
  CC9
  CC2
  CC3
EX
ID
IF
MEM
EX
ID
IF
lw $t6, 8($s5)
ori $t4, $s3, 7
sub $t5, $s2, $s3
sw $s2, 10($s3)
Instructions
Structural Hazard
Two instructions are attempting to write the register file during same cycle

## Slide 27: Resolving Structural Hazards
Serious Hazard:
  Hazard cannot be ignored
Solution 1: Delay Access to Resource
  Must have mechanism to delay instruction access to resource
  Delay all write backs to the register file to stage 5
    ALU instructions bypass stage 4 (memory) without doing anything
Solution 2: Add more hardware resources (more costly)
  Add more hardware to eliminate the structural hazard
  Redesign the register file to have two write ports
    First write port can be used to write back ALU results in stage 4
    Second write port can be used to write back load data in stage 5

## Slide 28: Data Hazards
Dependency between instructions causes a data hazard
The dependent instructions are close to each other
  Pipelined execution might change the order of operand access
Read After Write – RAW Hazard
  Given two instructions I and J, where I comes before J
  Instruction J should read an operand after it is written by I
  Called a data dependence in compiler terminology
  I: add $s1, $s2, $s3 # $s1 is written
  J: sub $s4, $s1, $s3 # $s1 is read
  Hazard occurs when J reads the operand before I writes it

## Slide 29: Example of a RAW Data Hazard
DM
Reg
IM
Reg
ALU
IM
DM
Reg
Reg
ALU
IM
DM
Reg
Reg
ALU
DM
Reg
ALU
Reg
DM
IM
Reg
ALU
IM
Time (cycles)
Program Execution Order
value of $s2
sub $s2, $t1, $t3
CC1
10
CC2
add $s4, $s2, $t5
10
CC3
or $s6, $t3, $s2
10
CC4
and $s7, $t4, $s2
10
CC6
20
CC7
20
CC8
20
CC5
sw $t8, 10($s2)
10
Result of sub is needed by add, or, and, & sw instructions
Instructions add & or will read old value of $s2 from reg file
During CC5, $s2 is written at end of cycle, old value is read

## Slide 30: Solution 1: Stalling the Pipeline
Reg
Reg
Three stall cycles during CC3 thru CC5 (wasting 3 cycles)
  The 3 stall cycles delay the execution of add and the fetching of or
  The 3 stall cycles insert 3 bubbles (No operations) into the ALU
The add instruction remains in the second stage until CC6
The or instruction is not fetched until CC6
DM
Reg
Reg
Reg
Time (in cycles)
Instruction Order
value of $s2
CC1
10
CC2
10
CC3
10
CC4
10
CC6
20
CC7
20
CC8
20
CC5
10
add $s4, $s2, $t5
IM
or $s6, $t3, $s2
IM
ALU
ALU
Reg
sub $s2, $t1, $t3
IM
Reg
ALU
DM
Reg
CC9
20
DM
stall
stall
stall

## Slide 31: Solution 2: Forwarding ALU Result
DM
Reg
Reg
Reg
Reg
Reg
Time (cycles)
Program Execution Order
value of $s2
sub $s2, $t1, $t3
IM
CC1
10
CC2
add $s4, $s2, $t5
IM
10
CC3
or $s6, $t3, $s2
ALU
IM
10
CC4
and $s7, $s6, $s2
ALU
IM
10
CC6
Reg
DM
ALU
20
CC7
Reg
DM
ALU
20
CC8
Reg
DM
20
CC5
sw $t8, 10($s2)
Reg
DM
ALU
IM
10
The ALU result is forwarded (fed back) to the ALU input
  No bubbles are inserted into the pipeline and no cycles are wasted
ALU result is forwarded from ALU, MEM, and WB stages

## Slide 32: Implementing Forwarding
0
1
2
3
0
1
2
3
R
32
32
clk
32
Rs
Instruction
0
1
ALU result
32
0
1
Data
Memory
Address
Data_in
Data_out
32
Rd4
A
L
U
Ext
Imm16
1
0
Rd3
Rd2
A
B
Data
D
Imm
32
Register File
RB
BusA
BusB
RW
BusW
RA
Rt
Two multiplexers added at the inputs of A & B registers
  Data from ALU stage, MEM stage, and WB stage is fed back
Two signals: ForwardA and ForwardB to control forwarding
ForwardA
ForwardB
32
Rd

## Slide 33: Forwarding Control Signals
Signal | Explanation
ForwardA = 0 | First ALU operand comes from register file = Value of (Rs)
ForwardA = 1 | Forward result of previous instruction to A (from ALU stage)
ForwardA = 2 | Forward result of 2nd previous instruction to A (from MEM stage)
ForwardA = 3 | Forward result of 3rd previous instruction to A (from WB stage)
ForwardB = 0 | Second ALU operand comes from register file = Value of (Rt)
ForwardB = 1 | Forward result of previous instruction to B (from ALU stage)
ForwardB = 2 | Forward result of 2nd previous instruction to B (from MEM stage)
ForwardB = 3 | Forward result of 3rd previous instruction to B (from WB stage)

## Slide 34: Forwarding Example
0
1
2
3
0
1
2
3
R
32
32
clk
32
Rs
Instruction
0
1
ALU result
32
0
1
Data
Memory
Address
Data_in
Data_out
32
Rd4
A
L
U
Ext
Imm16
1
0
Rd3
Rd2
A
B
Data
D
Imm
32
Register File
RB
BusA
BusB
RW
BusW
RA
Rt
32
Rd
Instruction sequence:
lw $t4, 4($t0)
ori $t7, $t1, 2
sub $t3, $t4, $t7
When sub instruction in ID stage
ori will be in the ALU stage
lw will be in the MEM stage
lw $t4,4($t0)
ori $t7,$t1,2
sub $t3,$t4,$t7
ForwardA = 2 (from MEM stage)
ForwardB = 1 (from ALU stage)

## Slide 35: RAW Hazard Detection
Current instruction is being decoded in the Decode stage
Previous instruction is in the Execute stage
Second previous instruction is in the Memory stage
Third previous instruction is in the Write Back stage
If ((Rs != 0) and (Rs == Rd2) and (EX.RegWr)) ForwardA = 1
Else if ((Rs != 0) and (Rs == Rd3) and (MEM.RegWr)) ForwardA = 2
Else if ((Rs != 0) and (Rs == Rd4) and (WB.RegWr)) ForwardA = 3
Else ForwardA = 0
If ((Rt != 0) and (Rt == Rd2) and (EX.RegWr)) ForwardB = 1
Else if ((Rt != 0) and (Rt == Rd3) and (MEM.RegWr)) ForwardB = 2
Else if ((Rt != 0) and (Rt == Rd4) and (WB.RegWr)) ForwardB = 3
Else ForwardB = 0

## Slide 36: Hazard Detecting and Forwarding Logic
ForwardB
ForwardA
Rs
Rt
Hazard
Detect &
Forward
0
1
2
3
0
1
2
3
R
32
32
clk
32
Rs
Instruction
0
1
ALU result
32
0
1
Data
Memory
Address
Data_in
Data_out
32
Rd4
A
L
U
Ext
Imm16
1
0
Rd3
Rd2
A
B
Data
D
Imm
32
Register File
RB
BusA
BusB
RW
BusW
RA
Rt
32
Rd
Main
& ALU
Control
Op
func
WB
RegDst
EX
ExtOp
ExtOp
ALUSrc
ALUOp
MEM
MemRd
MemWr
WBdata
RegWr
RegWr
RegWr

## Slide 37: Next . . .
Serial versus Pipelined Execution
Pipelined Datapath and Control
Pipeline Hazards
Data Hazards and Forwarding
Load Delay, Hazard Detection, and Stall
Control Hazards

## Slide 38: Load Delay
Reg
Reg
Reg
Time (cycles)
Program Order
CC2
add $s4, $s2, $t5
Reg
IF
CC3
or $t6, $t3, $s2
ALU
IF
CC6
Reg
DM
ALU
CC7
Reg
Reg
DM
CC8
Reg
lw $s2, 20($t1)
IF
CC1
CC4
and $t7, $s2, $t4
DM
ALU
IF
CC5
DM
ALU
Unfortunately, not all data hazards can be forwarded
  Load has a delay that cannot be eliminated by forwarding
In the example shown below …
  The LW instruction does not read data until end of CC4
  Cannot forward data to ADD at end of CC3 - NOT possible
However, load can forward data to 2nd next and later instructions

## Slide 39: Detecting RAW Hazard after Load
Detecting a RAW hazard after a Load instruction:
  The load instruction will be in the EX stage
  Instruction that depends on the load data is in the decode stage
Condition for stalling the pipeline
  if ((EX.MemRd == 1) // Detect Load in EX stage
  and (ForwardA==1 or ForwardB==1)) Stall // RAW Hazard
Insert a bubble into the EX stage after a load instruction
  Bubble is a no-op that wastes one clock cycle
  Delays the dependent instruction after load by one cycle
    Because of RAW hazard

## Slide 40: Stall the Pipeline for one Cycle
Reg
or $t6, $s3, $s2
IM
DM
Reg
ALU
Reg
ALU
DM
Reg
add $s4, $s2, $t5
IM
Reg
lw $s2, 20($s1)
IM
stall
ALU
bubble
bubble
bubble
DM
Reg
ADD instruction depends on LW  stall at CC3
  Allow Load instruction in ALU stage to proceed
  Freeze PC and Instruction registers (NO instruction is fetched)
  Introduce a bubble into the ALU stage (bubble is a NO-OP)
Load can forward data to next instruction after delaying it
Time (cycles)
Program Order
CC2
CC3
CC6
CC7
CC8
CC1
CC4
CC5

## Slide 41: Showing Stall Cycles
lw $s2, 8($s1)
MEM
WB
EX
ID
Stall
IF
lw $s1, ($t5)
MEM
WB
EX
ID
IF
Stall cycles can be shown on instruction-time diagram
Hazard is detected in the Decode stage
Stall indicates that instruction is delayed
Instruction fetching is also delayed after a stall
Example:
add $v0, $s2, $t3
-
WB
EX
ID
Stall
IF
sub $v1, $s2, $v0
-
WB
EX
ID
IF
  Time
  CC1
  CC4
  CC5
  CC6
  CC7
  CC8
  CC9
  CC2
  CC3
  CC10
Data forwarding is shown using green arrows

## Slide 42: Hazard Detecting and Forwarding Logic
ForwardB
ForwardA
Rs
Rt
Hazard Detect
Forward
and Stall
MemRd
RegWr
RegWr
RegWr
Stall
Disable PC
Disable IR
Bubble = 0
0
1
2
3
0
1
2
3
R
32
32
clk
32
Rs
Instruction
0
1
ALU result
32
0
1
Data
Memory
Address
Data_in
Data_out
32
Rd4
A
L
U
Ext
Imm16
1
0
Rd3
Rd2
A
B
Data
D
Imm
32
Register File
RB
BusA
BusB
RW
BusW
RA
Rt
32
Rd
Main
& ALU
Control
Op
func
WB
MemRd
MemWr
WBdata
RegDst
EX
ExtOp
MEM
PC
Control Signals
0
1
ALUSrc
ALUOp

## Slide 43: Code Scheduling to Avoid Stalls
Compilers reorder code in a way to avoid load stalls
Consider the translation of the following statements:
  A = B + C; D = E – F; // A thru F are in Memory
Slow code:
  lw $t0, 4($s0) # &B = 4($s0)
  lw $t1, 8($s0) # &C = 8($s0)
  add $t2, $t0, $t1 # stall cycle
  sw $t2, 0($s0) # &A = 0($s0)
  lw $t3, 16($s0) # &E = 16($s0)
  lw $t4, 20($s0) # &F = 20($s0)
  sub $t5, $t3, $t4 # stall cycle
  sw $t5, 12($0) # &D = 12($0)
Fast code: No Stalls
  lw $t0, 4($s0)
  lw $t1, 8($s0)
  lw $t3, 16($s0)
  lw $t4, 20($s0)
  add $t2, $t0, $t1
  sw $t2, 0($s0)
  sub $t5, $t3, $t4
  sw $t5, 12($s0)

## Slide 44: Name Dependence: Write After Read
Instruction J should write its result after it is read by I
Called anti-dependence by compiler writers
I: sub $t4, $t1, $t3 # $t1 is read
J: add $t1, $t2, $t3 # $t1 is written
Results from reuse of the name $t1
NOT a data hazard in the 5-stage pipeline because:
  Reads are always in stage 2
  Writes are always in stage 5, and
  Instructions are processed in order
Anti-dependence can be eliminated by renaming
  Use a different destination register for add (eg, $t5)

## Slide 45: Name Dependence: Write After Write
Same destination register is written by two instructions
Called output-dependence in compiler terminology
I: sub $t1, $t4, $t3 # $t1 is written
J: add $t1, $t2, $t3 # $t1 is written again
Not a data hazard in the 5-stage pipeline because:
  All writes are ordered and always take place in stage 5
However, can be a hazard in more complex pipelines
  If instructions are allowed to complete out of order, and
  Instruction J completes and writes $t1 before instruction I
Output dependence can be eliminated by renaming $t1
Read After Read is NOT a name dependence

## Slide 46: Next . . .
Serial versus Pipelined Execution
Pipelined Datapath and Control
Pipeline Hazards
Data Hazards and Forwarding
Load Delay, Hazard Detection, and Stall
Control Hazards

## Slide 47: Control Hazards
Jump and Branch can cause great performance loss
Jump instruction needs only the jump target address
Branch instruction needs two things:
  Branch Result Taken or Not Taken
  Branch Target Address
    PC + 4 If Branch is NOT taken
    PC + 4 + 4 × immediate If Branch is Taken
Jump and Branch targets are computed in the ID stage
  At which point a new instruction is already being fetched
  Jump Instruction: 1-cycle delay
  Branch: 2-cycle delay for branch result (taken or not taken)

## Slide 48: 1-Cycle Jump Delay
Control logic detects a Jump instruction in the 2nd Stage
Next instruction is fetched anyway
Convert Next instruction into bubble (Jump is always taken)
J L1
IF
cc1
Next instruction
. . .
L1: Target instruction
cc2
ID
IF
Jump
Target
Addr
cc4
cc5
cc6
cc7
cc3
Bubble
Bubble
Bubble
Bubble
IF
Reg
DM
ALU
Reg

## Slide 49: 2-Cycle Branch Delay
Control logic detects a Branch instruction in the 2nd Stage
ALU computes the Branch outcome in the 3rd Stage
Next1 and Next2 instructions will be fetched anyway
Convert Next1 and Next2 into bubbles if branch is taken
Beq $t1,$t2,L1
IF
cc1
Next1
cc2
Reg
IF
Next2
cc4
cc5
cc6
cc7
IF
Reg
DM
ALU
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
L1: target instruction
cc3
Branch
Target
Addr
ALU
Reg
IF

## Slide 50: If Branch is NOT Taken . . .
Branches can be predicted to be NOT taken
If branch outcome is NOT taken then
  Next1 and Next2 instructions can be executed
  Do not convert Next1 & Next2 into bubbles
  No wasted cycles
Beq $t1,$t2,L1
IF
cc1
Next1
cc2
Reg
IF
Next2
cc3
NOT Taken
ALU
Reg
IF
Reg
cc4
cc5
cc6
cc7
ALU
DM
ALU
DM
Reg
Reg

## Slide 51: Pipelined Jump and Branch
J
J
Main
& ALU
Control
Op
func
ForwardB
ForwardA
Rs
Rt
Forward & Stall
Rd2, Rd3, Rd4
RegWr, MemRd
0
1
2
3
0
1
2
3
R
32
32
Rs
Instruction
0
1
A
L
U
Ext
Imm16
1
0
Rd3
Rd2
A
B
D
Imm
32
Register File
RB
BusA
BusB
RW
BusW
RA
Rt
32
Rd
Zero
Address
Instruction
Instruction
Memory
Branch Target Address
Jump Target = PC[31:28] ‖ Imm26
Next PC Address
+
0
1
2
+1
PC
00
NPC
BTA
0
1
Bubble = 0
Stall
Disable PC
Disable IR
Bubble = NOP
Kill1
Jump
kills next
instruction
Kill2
Taken branch kills two
MEM
Control Signals
0
1
Control Signals
EX
PC
Control
PCSrc
BEQ, BNE
BEQ, BNE
Zero

## Slide 52: PC Control for Pipelined Jump and Branch
if ((BEQ && Zero) || (BNE && !Zero))
{ Jmp=0; Br=1; Kill1=1; Kill2=1; }
else if (J)
{ Jmp=1; Br=0; Kill1=1; Kill2=0; }
else
{ Jmp=0; Br=0; Kill1=0; Kill2=0; }
Br = (( BEQ · Zero ) + (BNE · Zero ))
Jmp = J · Br
Kill1 = J + Br
Kill2 = Br
PCSrc = { Br, Jmp } // 0, 1, or 2
Br
Jmp
Kill1
Kill2
BEQ
BNE
J
Zero
PCSrc

## Slide 53: Jump and Branch Impact on CPI
Base CPI = 1 without counting jump and branch
Unconditional Jump = 5%, Conditional branch = 20%
90% of conditional branches are taken
Jump kills next instruction, Taken Branch kills next two
What is the effect of jump and branch on the CPI?
Solution:
Jump adds 1 wasted cycle for 5% of instructions = 1 × 0.05
Branch adds 2 wasted cycles for 20% × 90% of instructions
= 2 × 0.2 × 0.9 = 0.36
New CPI = 1 + 0.05 + 0.36 = 1.41 (due to wasted cycles)