## Slide 1: Introduction to Assembly Language Programming
COE 301
Computer Organization
Prof. Muhamed Mudawar
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
System Calls
Defining Data
Memory Alignment and Byte Ordering

## Slide 3: Instruction Set Architecture (ISA)
Critical Interface between software and hardware
An ISA includes the following …
  Instructions and Instruction Formats
  Data Types, Encodings, and Representations
  Programmable Storage: Registers and Memory
  Addressing Modes: to address Instructions and Data
  Handling Exceptional Conditions (like overflow)
Examples (Versions) Introduced in
  Intel (8086, 80386, Pentium, Core, ...) 1978
  MIPS (MIPS I, II, …, MIPS32, MIPS64) 1986
  ARM (version 1, 2, …) 1985

## Slide 4: Instructions
Instructions are the language of the machine
We will study the MIPS instruction set architecture
  Known as Reduced Instruction Set Computer (RISC)
  Elegant and relatively simple design
  Similar to RISC architectures developed in mid-1980’s and 90’s
  Popular, used in many products
    Silicon Graphics, ATI, Cisco, Sony, etc.
Alternative to: Intel x86 architecture
  Known as Complex Instruction Set Computer (CISC)

## Slide 5: Overview of the MIPS Architecture
Memory
Up to 232 bytes = 230 words
4 bytes per word
$0
$1
$2
$31
Hi
Lo
ALU
F0
F1
F2
F31
FP
Arith
EPC
Cause
BadVaddr
Status
EIU
FPU
TMU
Execution &
Integer Unit
(Main proc)
Floating
Point Unit
(Coproc 1)
Trap &
Memory Unit
(Coproc 0)
. . .
. . .
Integer
mul/div
Arithmetic &
Logic Unit
32 General
Purpose
Registers
Integer Multiplier/Divider
32 Floating-Point
Registers
Floating-Point
Arithmetic Unit

## Slide 6: MIPS General-Purpose Registers
32 General Purpose Registers (GPRs)
  All registers are 32-bit wide in the MIPS 32-bit architecture
  Software defines names for registers to standardize their use
  Assembler can refer to registers by name or by number ($ notation)
Name | Register | Usage
$zero | $0 | Always 0 (forced by hardware)
$at | $1 | Reserved for assembler use
$v0 – $v1 | $2 – $3 | Result values of a function
$a0 – $a3 | $4 – $7 | Arguments of a function
$t0 – $t7 | $8 – $15 | Temporary Values
$s0 – $s7 | $16 – $23 | Saved registers (preserved across call)
$t8 – $t9 | $24 – $25 | More temporaries
$k0 – $k1 | $26 – $27 | Reserved for OS kernel
$gp | $28 | Global pointer (points to global data)
$sp | $29 | Stack pointer (points to top of stack)
$fp | $30 | Frame pointer (points to stack frame)
$ra | $31 | Return address (used by jal for function call)

## Slide 7: Instruction Formats
All instructions are 32-bit wide, Three instruction formats:
Register (R-Type)
  Register-to-register instructions
  Op: operation code specifies the format of the instruction
Immediate (I-Type)
  16-bit immediate constant is part in the instruction
Jump (J-Type)
  Used by jump instructions
Op6
Rs5
Rt5
Rd5
funct6
sa5
Op6
Rs5
Rt5
immediate16
Op6
immediate26

## Slide 8: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
System Calls
Defining Data
Memory Alignment and Byte Ordering

## Slide 9: What is Assembly Language?
Low-level programming language for a computer
One-to-one correspondence with the machine instructions
Assembly language is specific to a given processor
Assembler: converts assembly program into machine code
Assembly language uses:
  Mnemonics: to represent the names of low-level machine instructions
  Labels: to represent the names of variables or memory addresses
  Directives: to define data and constants
  Macros: to facilitate the inline expansion of text into other code

## Slide 10: Assembly Language Statements
Three types of statements in assembly language
  Typically, one statement should appear on a line
Executable Instructions
  Generate machine code for the processor to execute at runtime
  Instructions tell the processor what to do
Pseudo-Instructions and Macros
  Translated by the assembler into real instructions
  Simplify the programmer task
Assembler Directives
  Provide information to the assembler while translating a program
  Used to define segments, allocate memory variables, etc.
  Non-executable: directives are not part of the instruction set

## Slide 11: Assembly Language Instructions
Assembly language instructions have the format:
[label:] mnemonic [operands] [#comment]
Label: (optional)
  Marks the address of a memory location, must have a colon
  Typically appear in data and text segments
Mnemonic
  Identifies the operation (e.g. add, sub, etc.)
Operands
  Specify the data required by the operation
  Operands can be registers, memory variables, or constants
  Most instructions have three operands
L1: addiu $t0, $t0, 1 #increment $t0

## Slide 12: Comments
Single-line comment
  Begins with a hash symbol # and terminates at end of line
Comments are very important!
  Explain the program's purpose
  When it was written, revised, and by whom
  Explain data used in the program, input, and output
  Explain instruction sequences and algorithms used
  Comments are also required at the beginning of every procedure
    Indicate input parameters and results of a procedure
    Describe what the procedure does

## Slide 13: Program Template
# Title: Filename:
# Author: Date:
# Description:
# Input:
# Output:
################# Data segment #####################
.data
. . .
################# Code segment #####################
.text
.globl main
main: # main program entry
. . .
li $v0, 10 # Exit program
syscall

## Slide 14: .DATA, .TEXT, & .GLOBL Directives
.DATA directive
  Defines the data segment of a program containing data
  The program's variables should be defined under this directive
  Assembler will allocate and initialize the storage of variables
.TEXT directive
  Defines the code segment of a program containing instructions
.GLOBL directive
  Declares a symbol as global
  Global symbols can be referenced from other files
  We use this directive to declare main function of a program

## Slide 15: Layout of a Program in Memory
Stack Segment
0x7FFFFFFF
Dynamic Area (Heap)
Static Area
Text Segment
Reserved
0x04000000
0x10000000
0
Data Segment
Memory
Addresses
in Hex
Stack Grows
Downwards
Instructions
appear here
Static data
appear here

## Slide 16: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
System Calls
Defining Data
Memory Alignment and Byte Ordering

## Slide 17: System Calls
Programs do input/output through system calls
The MIPS architecture provides a syscall instruction
  To obtain services from the operating system
  The operating system handles all system calls requested by program
Since MARS is a simulator, it simulates the syscall services
To use the syscall services:
  Load the service number in register $v0
  Load argument values, if any, in registers $a0, $a1, etc.
  Issue the syscall instruction
  Retrieve return values, if any, from result registers

## Slide 18: Syscall Services
Service | $v0 | Arguments / Result
Print Integer | 1 | $a0 = integer value to print
Print Float | 2 | $f12 = float value to print
Print Double | 3 | $f12 = double value to print
Print String | 4 | $a0 = address of null-terminated string
Read Integer | 5 | Return integer value in $v0
Read Float | 6 | Return float value in $f0
Read Double | 7 | Return double value in $f0
Read String | 8 | $a0 = address of input buffer $a1 = maximum number of characters to read
Allocate Heap memory | 9 | $a0 = number of bytes to allocate Return address of allocated memory in $v0
Exit Program | 10 | 

## Slide 19: Syscall Services – Cont’d
Print Char | 11 | $a0 = character to print
Read Char | 12 | Return character read in $v0
Open File | 13 | $a0 = address of null-terminated filename string $a1 = flags (0 = read-only, 1 = write-only) $a2 = mode (ignored) Return file descriptor in $v0 (negative if error)
Read from File | 14 | $a0 = File descriptor $a1 = address of input buffer $a2 = maximum number of characters to read Return number of characters read in $v0
Write to File | 15 | $a0 = File descriptor $a1 = address of buffer $a2 = number of characters to write Return number of characters written in $v0
Close File | 16 | $a0 = File descriptor

## Slide 20: Reading and Printing an Integer
################# Code segment #####################
.text
.globl main
main: # main program entry
li $v0, 5 # Read integer
syscall # $v0 = value read
move $a0, $v0 # $a0 = value to print
li $v0, 1 # Print integer
syscall
li $v0, 10 # Exit program
syscall

## Slide 21: Reading and Printing a String
################# Data segment #####################
.data
str: .space 10 # array of 10 bytes
################# Code segment #####################
.text
.globl main
main: # main program entry
la $a0, str # $a0 = address of str
li $a1, 10 # $a1 = max string length
li $v0, 8 # read string
syscall
li $v0, 4 # Print string str
syscall
li $v0, 10 # Exit program
syscall

## Slide 22: Sum of Three Integers
# Sum of three integers
# Objective: Computes the sum of three integers.
# Input: Requests three numbers, Output: sum
################### Data segment ###################
.data
prompt: .asciiz "Please enter three numbers: \n"
sum_msg: .asciiz "The sum is: "
################### Code segment ###################
.text
.globl main
main:
la $a0,prompt # display prompt string
li $v0,4
syscall
li $v0,5 # read 1st integer into $t0
syscall
move $t0,$v0

## Slide 23: Sum of Three Integers – (cont'd)
li $v0,5 # read 2nd integer into $t1
syscall
move $t1,$v0
li $v0,5 # read 3rd integer into $t2
syscall
move $t2,$v0
addu $t0,$t0,$t1 # accumulate the sum
addu $t0,$t0,$t2
la $a0,sum_msg # write sum message
li $v0,4
syscall
move $a0,$t0 # output sum
li $v0,1
syscall
li $v0,10 # exit
syscall

## Slide 24: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
System Calls
Defining Data
Memory Alignment and Byte Ordering

## Slide 25: Data Definition Statement
The assembler uses directives to define data
It allocates storage in the static data segment for a variable
May optionally assign a name (label) to the data
Syntax:
[name:] directive initializer [, initializer] . . .
  var1: .WORD 10
All initializers become binary data in memory

## Slide 26: Data Directives
.BYTE Directive
  Stores the list of values as 8-bit bytes
.HALF Directive
  Stores the list as 16-bit values aligned on half-word boundary
.WORD Directive
  Stores the list as 32-bit values aligned on a word boundary
.FLOAT Directive
  Stores the listed values as single-precision floating point
.DOUBLE Directive
  Stores the listed values as double-precision floating point

## Slide 27: String Directives
.ASCII Directive
  Allocates a sequence of bytes for an ASCII string
.ASCIIZ Directive
  Same as .ASCII directive, but adds a NULL char at end of string
  Strings are null-terminated, as in the C programming language
.SPACE Directive
  Allocates space of n uninitialized bytes in the data segment

## Slide 28: Examples of Data Definitions
.DATA
var1: .BYTE 'A', 'E', 127, -1, '\n'
var2: .HALF -10, 0xffff
var3: .WORD 0x12345678:100
var4: .FLOAT 12.3, -0.1
var5: .DOUBLE 1.5e-10
str1: .ASCII "A String\n"
str2: .ASCIIZ "NULL Terminated String"
array: .SPACE 100
Array of 100 words
Initialized with
the same value
100 bytes (not initialized)

## Slide 29: Next . . .
The MIPS Instruction Set Architecture
Introduction to Assembly Language
System Calls
Defining Data
Memory Alignment and Byte Ordering

## Slide 30: Memory Alignment
Memory is viewed as an addressable array of bytes
Byte Addressing: address points to a byte in memory
However, words occupy 4 consecutive bytes in memory
  MIPS instructions and integers occupy 4 bytes
Memory Alignment:
  Address must be multiple of size
  Word address should be a multiple of 4
  Double-word address should be a multiple of 8
.ALIGN n directive
  Aligns the next data definition on a 2n byte boundary
  Forces the address of next data definition to be multiple of 2n
0
4
8
12
address
not aligned
. . .
aligned word
not aligned
Memory

## Slide 31: Byte Ordering (Endianness)
Processors can order bytes within a word in two ways
Little Endian Byte Ordering
  Memory address = Address of least significant byte
  Example: Intel IA-32
Big Endian Byte Ordering
  Memory address = Address of most significant byte
  Example: SPARC architecture
MIPS can operate with both byte orderings
Byte 0
Byte 1
Byte 2
Byte 3
32-bit Register
MSB
LSB
. . .
. . .
Byte 0
Byte 1
Byte 2
Byte 3
a
a+3
a+2
a+1
Memory
address
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
32-bit Register
MSB
LSB
. . .
. . .
Byte 0
Byte 1
Byte 2
a
a+3
a+2
a+1
Memory
address

## Slide 32: Symbol Table
Assembler builds a symbol table for labels
  Assembler computes the address of each label in data segment
Example Symbol Table
.DATA
var1: .BYTE 1, 2,'Z'
str1: .ASCIIZ "My String\n"
var2: .WORD 0x12345678
.ALIGN 3
var3: .HALF 1000
Label
var1
str1
var2
var3
Address
0x10010000
0x10010003
0x10010010
0x10010018
var1
1
2
'Z'
0x10010000
str1
'M'
'y'
' '
'S'
't'
'r'
'i'
'n'
'g'
'\n'
0
0x12345678
0x10010010
var2 (aligned)
1000
var3 (address is multiple of 8)
0
0
Unused
0
0
0
0
Unused