## Slide 1: Data Representation
COE 301
Computer Organization
Prof. Muhamed Mudawar
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Positional Number Systems
Binary and Hexadecimal Numbers
Base Conversions
Integer Storage Sizes
Binary and Hexadecimal Addition
Signed Integers and 2's Complement Notation
Sign Extension
Binary and Hexadecimal subtraction
Carry and Overflow
Character Storage

## Slide 3: Positional Number Systems
Different Representations of Natural Numbers
XXVII Roman numerals (not positional)
27 Radix-10 or decimal number (positional)
110112 Radix-2 or binary number (also positional)
Fixed-radix positional representation with k digits
Number N in radix r = (dk–1dk–2 . . . d1d0)r
Value = dk–1×r k–1 + dk–2×r k–2 + … + d1×r + d0
Examples: (11011)2 = 1×24 + 1×23 + 0×22 + 1×2 + 1 = 27
(2103)4 = 2×43 + 1×42 + 0×4 + 3 = 147

## Slide 4: Binary Numbers
Each binary digit (called bit) is either 1 or 0
Bits have no inherent meaning, can represent
  Unsigned and signed integers
  Characters
  Floating-point numbers
  Images, sound, etc.
Bit Numbering
  Least significant bit (LSB) is rightmost (bit 0)
  Most significant bit (MSB) is leftmost (bit 7 in an 8-bit number)
1
0
0
1
1
1
0
1
2
7
2
6
2
5
2
4
2
3
2
2
2
1
2
0
0
1
2
3
4
5
6
7
Most
Significant Bit
Least
Significant Bit

## Slide 5: Converting Binary to Decimal
Each bit represents a power of 2
Every binary number is a sum of powers of 2
Decimal Value = (dn-1  2n-1) + ... + (d1  21) + (d0  20)
Binary (10011101)2 = 27 + 24 + 23 + 22 + 1 = 157
1
0
0
1
1
1
0
1
2
7
2
6
2
5
2
4
2
3
2
2
2
1
2
0
0
1
2
3
4
5
6
7
Some common powers of 2

## Slide 6: Convert Unsigned Decimal to Binary
Repeatedly divide the decimal integer by 2
Each remainder is a binary digit in the translated value
37 = (100101)2
least significant bit
most significant bit
stop when quotient is zero

## Slide 7: Hexadecimal Integers
16 Hexadecimal Digits: 0 – 9, A – F
More convenient to use than binary numbers
Binary, Decimal, and Hexadecimal Equivalents

## Slide 8: Converting Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits
Example:
Convert the 32-bit binary number to hexadecimal
1110 1011 0001 0110 1010 0111 1001 0100
Solution:
0100
4
1001
9
0111
7
1010
A
0110
6
0001
1
1011
B
1110
E

## Slide 9: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16
Value = (dn-1  16n-1) + (dn-2  16n-2) + ... + (d1  16) + d0
Examples:
(1234)16 = (1  163) + (2  162) + (3  16) + 4 =
Decimal Value 4660
(3BA4)16 = (3  163) + (11  162) + (10  16) + 4 =
Decimal Value 15268

## Slide 10: Converting Decimal to Hexadecimal
Decimal 422 = 1A6 hexadecimal
stop when quotient is zero
least significant digit
most significant digit
Repeatedly divide the decimal integer by 16
Each remainder is a hex digit in the translated value

## Slide 11: Integer Storage Sizes
What is the largest 20-bit unsigned integer?
Answer: 220 – 1 = 1,048,575
Storage Type | Unsigned Range | Powers of 2
Byte | 0 to 255 | 0 to (28 – 1)
Half Word | 0 to 65,535 | 0 to (216 – 1)
Word | 0 to 4,294,967,295 | 0 to (232 – 1)
Double Word | 0 to 18,446,744,073,709,551,615 | 0 to (264 – 1)
Byte
8
16
32
64
Half Word
Word
Double Word
Storage Sizes

## Slide 12: Binary Addition
Start with the least significant bit (rightmost bit)
Add each pair of bits
Include the carry in the addition, if present
0
0
0
1
1
1
0
1
0
0
1
1
0
1
1
0
+
(54)
(29)
(83)
1
carry
0
1
2
3
4
bit position:
5
6
7
1
1
1
0
1
0
1
0
0
1
1

## Slide 13: Hexadecimal Addition
Start with the least significant hexadecimal digits
Let Sum = summation of two hex digits
If Sum is greater than or equal to 16
  Sum = Sum – 16 and Carry = 1
Example:
A
F
C
D
B
0
1
1
1
1
C
3
7
2
8
6
A
9
3
9
5
E
8
4
B
+
A + B = 10 + 11 = 21
Since 21 ≥ 16
Sum = 21 – 16 = 5
Carry = 1
5
1
carry:

## Slide 14: Signed Integers
Several ways to represent a signed number
  Sign-Magnitude
  Biased
  1's complement
  2's complement
Divide the range of values into 2 equal parts
  First part corresponds to the positive numbers (≥ 0)
  Second part correspond to the negative numbers (< 0)
Focus will be on the 2's complement representation
  Has many advantages over other representations
  Used widely in processors to represent signed integers

## Slide 15: Two's Complement Representation
8-bit Binary value | Unsigned value | Signed value
00000000 | 0 | 0
00000001 | 1 | +1
00000010 | 2 | +2
. . . | . . . | . . .
01111110 | 126 | +126
01111111 | 127 | +127
10000000 | 128 | -128
10000001 | 129 | -127
. . . | . . . | . . .
11111110 | 254 | -2
11111111 | 255 | -1
Positive numbers
  Signed value = Unsigned value
Negative numbers
  Signed value = Unsigned value – 2n
  n = number of bits
Negative weight for MSB
  Another way to obtain the signed value is to assign a negative weight to most-significant bit
  = -128 + 32 + 16 + 4 = -76
1
0
1
1
0
1
0
0
-128
64
32
16
8
4
2
1

## Slide 16: Forming the Two's Complement
Sum of an integer and its 2's complement must be zero:
00100100 + 11011100 = 00000000 (8-bit sum)  Ignore Carry
Another way to obtain the 2's complement:
Start at the least significant 1
Leave all the 0s to its right unchanged
Complement all the bits to its left
starting value | 00100100 = +36
step1: reverse the bits (1's complement) | 11011011
step 2: add 1 to the value from step 1 | + 1
sum = 2's complement representation | 11011100 = -36
Binary Value
= 00100 1 00
2's Complement
= 11011 1 00
least
significant 1

## Slide 17: Sign Bit
Highest bit indicates the sign
1 = negative
0 = positive
For Hexadecimal Numbers, check most significant digit
If highest digit is > 7, then value is negative
Examples: 8A and C5 are negative bytes
B1C42A00 is a negative word (32-bit signed integer)
1
1
1
1
0
1
1
0
0
0
0
0
1
0
1
0
Sign bit
Negative
Positive

## Slide 18: Sign Extension
Step 1: Move the number into the lower-significant bits
Step 2: Fill all the remaining higher bits with the sign bit
This will ensure that both magnitude and sign are correct
Examples
  Sign-Extend 10110011 to 16 bits
  Sign-Extend 01100010 to 16 bits
Infinite 0s can be added to the left of a positive number
Infinite 1s can be added to the left of a negative number
10110011 = -77
11111111 10110011 = -77
01100010 = +98
00000000 01100010 = +98

## Slide 19: Two's Complement of a Hexadecimal
To form the two's complement of a hexadecimal
  Subtract each hexadecimal digit from 15
  Add 1
Examples:
  2's complement of 6A3D = 95C2 + 1 = 95C3
  2's complement of 92F15AC0 = 6D0EA53F + 1 = 6D0EA540
  2's complement of FFFFFFFF = 00000000 + 1 = 00000001
No need to convert hexadecimal to binary

## Slide 20: Binary Subtraction
When subtracting A – B, convert B to its 2's complement
Add A to (–B)
0 1 0 0 1 1 0 1 0 1 0 0 1 1 0 1
0 0 1 1 1 0 1 0 1 1 0 0 0 1 1 0 (2's complement)
0 0 0 1 0 0 1 1 0 0 0 1 0 0 1 1 (same result)
Final carry is ignored, because
  Negative number is sign-extended with 1's
  You can imagine infinite 1's to the left of a negative number
  Adding the carry to the extended 1's produces extended zeros
–
+
borrow:
carry:
1
1
1
1
1
1
1

## Slide 21: Hexadecimal Subtraction
When a borrow is required from the digit to the left, then
Add 16 (decimal) to the current digit's value
Last Carry is ignored
Borrow:
-
5
7
6
C
F
4
1
B
7
4
2
A
E
9
3
8
E
2
4
2
1
B
D
2
16 + 5 = 21
1
1
1
E
B
D
4
1
2
1
+
5
7
6
C
F
4
1
B
9
B
D
5
1
6
C
7
(2's complement)
(same result)
Carry:
2
1
1
1
2
1

## Slide 22: Ranges of Signed Integers
For n-bit signed integers: Range is -2n–1 to (2n–1 – 1)
Positive range: 0 to 2n–1 – 1
Negative range: -2n–1 to -1
Practice: What is the range of signed values that may be stored in 20 bits?
Storage Type | Signed Range | Powers of 2
Byte | –128 to +127 | –27 to (27 – 1)
Half Word | –32,768 to +32,767 | –215 to (215 – 1)
Word | –2,147,483,648 to +2,147,483,647 | –231 to (231 – 1)
Double Word | –9,223,372,036,854,775,808 to +9,223,372,036,854,775,807 | –263 to (263 – 1)

## Slide 23: Carry and Overflow
Carry is important when …
  Adding or subtracting unsigned integers
  Indicates that the unsigned sum is out of range
  Either < 0 or >maximum unsigned n-bit value
Overflow is important when …
  Adding or subtracting signed integers
  Indicates that the signed sum is out of range
Overflow occurs when
  Adding two positive numbers and the sum is negative
  Adding two negative numbers and the sum is positive
  Can happen because of the fixed number of sum bits

## Slide 24: Carry and Overflow Examples
0
1
0
0
0
0
0
0
0
1
0
0
1
1
1
1
+
1
0
0
0
1
1
1
1
79
64
143
(-113)
Carry = 0 Overflow = 1
1
1
0
0
1
1
1
0
1
1
1
0
1
1
0
1
0
+
0
1
1
1
0
1
1
1
218 (-38)
157 (-99)
119
Carry = 1 Overflow = 1
1
1
1
We can have carry without overflow and vice-versa
Four cases are possible (Examples are 8-bit numbers)
1
1
1
1
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
0
0
1
1
1
15
248 (-8)
7
Carry = 1 Overflow = 0
1
1
1
1
1
0
0
0
0
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
1
0
1
1
1
15
8
23
Carry = 0 Overflow = 0
1

## Slide 25: Range, Carry, Borrow, and Overflow
Unsigned Integers: n-bit representation
Signed Integers: n-bit 2's complement representation
max = 2n–1
min = 0
Carry = 1
Addition
Numbers > max
Borrow = 1
Subtraction
Numbers < min
Positive
Overflow
Numbers > max
Negative
Overflow
Numbers < min
max = 2n-1–1
Finite Set of Signed Integers
0
min = -2n-1
Finite Set of Unsigned Integers

## Slide 26: Character Storage
Character sets
  Standard ASCII: 7-bit character codes (0 – 127)
  Extended ASCII: 8-bit character codes (0 – 255)
  Unicode: 16-bit character codes (0 – 65,535)
  Unicode standard represents a universal character set
    Defines codes for characters used in all major languages
    Used in Windows-XP: each character is encoded as 16 bits
  UTF-8: variable-length encoding used in HTML
    Encodes all Unicode characters
    Uses 1 byte for ASCII, but multiple bytes for other characters
Null-terminated String
  Array of characters followed by a NULL character

## Slide 27: Printable ASCII Codes
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
2 | space | ! | " | # | $ | % | & | ' | ( | ) | * | + | , | - | . | /
3 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | : | ; | < | = | > | ?
4 | @ | A | B | C | D | E | F | G | H | I | J | K | L | M | N | O
5 | P | Q | R | S | T | U | V | W | X | Y | Z | [ | \ | ] | ^ | _
6 | ` | a | b | c | d | e | f | g | h | i | j | k | l | m | n | o
7 | p | q | r | s | t | u | v | w | x | y | z | { | ¦ | } | ~ | DEL
Examples:
  ASCII code for space character = 20 (hex) = 32 (decimal)
  ASCII code for 'L' = 4C (hex) = 76 (decimal)
  ASCII code for 'a' = 61 (hex) = 97 (decimal)

## Slide 28: Control Characters
The first 32 characters of ASCII table are used for control
Control character codes = 00 to 1F (hexadecimal)
  Not shown in previous slide
Examples of Control Characters
  Character 0 is the NULL character  used to terminate a string
  Character 9 is the Horizontal Tab (HT) character
  Character 0A (hex) = 10 (decimal) is the Line Feed (LF)
  Character 0D (hex) = 13 (decimal) is the Carriage Return (CR)
  The LF and CR characters are used together
    They advance the cursor to the beginning of next line
One control character appears at end of ASCII table
  Character 7F (hex) is the Delete (DEL) character