## Slide 1: Integer Multiplication and Division
COE 301
Computer Organization
Prof. Muhamed Mudawar
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 3: Unsigned Integer Multiplication
Paper and Pencil Example:
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
n-bit multiplicand × n-bit multiplier = (2n)-bit product
Accomplished via shifting and addition
Consumes more time and more chip area than addition
Binary multiplication is easy
0 × multiplicand = 0
1 × multiplicand = multiplicand

## Slide 4: Unsigned Sequential Multiplication
Initialize Product = 0
Check each bit of the Multiplier
If Multiplier bit = 1 then Product = Product + Multiplicand
Rather than shifting the multiplicand to the left,
Shift the Product to the Right
Has the same net effect and produces the same result
Minimizes the hardware resources
One cycle per iteration (for each bit of the Multiplier)
  Addition and shifting can be done simultaneously

## Slide 5: Unsigned Sequential Multiplier
Initialize: HI = 0
Initialize: LO = Multiplier
Final Product in HI and LO registers
Repeat for each bit of Multiplier
= 0
Start
LO[0]?
Carry, Sum = HI + Multiplicand
32nd Repetition?
Done
= 1
No
Yes
HI = 0, LO=Multiplier
HI, LO = Shift Right (Carry, Sum, LO)
32-bit ALU
Control
64 bits
32 bits
write
add
LO[0]
Multiplicand
shift right
32 bits
HI
LO
Sum
Carry
32 bits

## Slide 6: Sequential Multiplier Example
Consider: 11002 × 11012 , Product = 100111002
4-bit multiplicand and multiplier are used in this example
4-bit adder produces a 4-bit Sum + Carry bit
1 1 0 0
Shift Right (Carry, Sum, LO) by 1 bit
0 1 1 1 1 0 0 1
LO[0] = 0 => NO addition
1 1 0 0
Shift Right (HI, LO) by 1 bit
0 0 1 1 0 0 1 1
1 1 0 0
Shift Right (Carry, Sum, LO) by 1 bit
0 1 1 0 0 1 1 0
1 1 0 0
Shift Right (Carry, Sum, LO) by 1 bit
1 0 0 1 1 1 0 0
2
1 1 0 0
0 0 0 0 1 1 0 1
Initialize (HI = 0, LO = Multiplier)
0
1
3
4
Multiplicand
Product = HI, LO
Carry
Iteration
0
1 1 0 0 1 1 0 1
LO[0] = 1 => ADD
+
0
1 1 1 1 0 0 1 1
LO[0] = 1 => ADD
+
1
0 0 1 1 1 0 0 1
LO[0] = 1 => ADD
+

## Slide 7: Next . . .
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 8: Signed Integer Multiplication
First attempt:
  Convert multiplier and multiplicand into positive numbers
    If negative then obtain the 2's complement and remember the sign
  Perform unsigned multiplication
  Compute the sign of the product
  If product sign < 0 then obtain the 2's complement of the product
  Drawback: additional steps to compute the 2's complement
Better version:
  Use the unsigned multiplication hardware
  When shifting right, extend the sign of the product
  If multiplier is negative, the last step should be a subtract

## Slide 9: Signed Multiplication (Paper & Pencil)
Case 1: Positive Multiplier
Multiplicand 11002 = -4
Multiplier × 01012 = +5
11111100
111100
Product 111011002 = -20
Case 2: Negative Multiplier
Multiplicand 11002 = -4
Multiplier × 11012 = -3
11111100
111100
00100 (2's complement of 1100)
Product 000011002 = +12
Sign-extension
Sign-extension

## Slide 10: Signed Sequential Multiplier
ALU produces: 32-bit sum + sign bit
Sign bit can be computed:
  No overflow: sign = sum[31]
  If Overflow: sign = ~sum[31]
= 0
Start
LO[0]?
31 iterations: Sign, Sum = HI + Multiplicand
Last iteration: Sign, Sum = HI – Multiplicand
32nd Repetition?
Done
= 1
No
Yes
HI = 0, LO = Multiplier
HI, LO = Shift Right (Sign, Sum, LO)
32-bit ALU
Control
64 bits
32 bits
write
add, sub
LO[0]
Multiplicand
shift right
32 bits
HI
LO
sum
sign
32 bits

## Slide 11: Signed Multiplication Example
Consider: 11002 (-4) × 11012 (-3), Product = 000011002
Check for overflow: No overflow  Extend sign bit
Last iteration: add 2's complement of Multiplicand
1 1 0 0
Shift Right (Sign, Sum, LO) by 1 bit
1 1 0 1 1 0 0 1
LO[0] = 0 => NO addition
1 1 0 0
Shift Right (Sign, HI, LO) by 1 bit
1 1 1 1 0 0 1 1
1 1 0 0
Shift Right (Sign, Sum, LO) by 1 bit
1 1 1 0 0 1 1 0
Shift Right (Sign, Sum, LO) by 1 bit
0 0 0 0 1 1 0 0
2
1 1 0 0
0 0 0 0 1 1 0 1
Initialize (HI = 0, LO = Multiplier)
0
1
3
4
Multiplicand
Product = HI, LO
Sign
Iteration
1
1 1 0 0 1 1 0 1
LO[0] = 1 => ADD
+
1
1 0 1 1 0 0 1 1
LO[0] = 1 => ADD
+
0 1 0 0
0
0 0 0 1 1 0 0 1
LO[0] = 1 => SUB (ADD 2's compl)
+

## Slide 12: Next . . .
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 13: Faster Multiplier
Suppose we want to multiply two numbers A and B
  Example on 4-bit numbers: A = a3 a2 a1 a0 and B = b3 b2 b1 b0
Step 1: AND (multiply) each bit of A with each bit of B
  Requires n2 AND gates and produces n2 product bits
  Position of aibj = (i+j). For example, Position of a2b3 = 2+3 = 5
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
a0b2
a1b2
a2b2
a3b2
a0b3
a1b3
a2b3
a3b3
A × B

## Slide 14: Adding the Partial Products
Step 2: Add the partial products
  The partial products are shifted and added to compute the product P
  The partial products can be added in parallel
  Different implementations are possible
4-bit Multiplicand A3 A2 A1 A0
4-bit Multiplier × B3 B2 B1 B0
A3B0 A2B0 A1B0 A0B0
A3B1 A2B1 A1B1 A0B1
A3B2 A2B2 A1B2 A0B2
A3B3 A2B3 A1B3 A0B3
P7 P6 P5 P4 P3 P2 P1 P0
8-bit Product
Partial Products are shifted
and added
Can be added
in parallel

## Slide 15: 4-bit × 4-bit Binary Multiplier
4-bit Adder
A3
0
A2
A1
A0
B0
A3
carry
A2
A1
A0
B1
4-bit Adder
A3
0
A2
A1
A0
B2
A3
A2
A1
A0
B3
4-bit Adder
carry
Half
Adder
carry
P0
P1
P4
P5
P2
P3
P6
P7
16 AND gates, Three 4-bit adders, a half-adder, and an OR gate

## Slide 16: Carry Save Adders
A n-bit carry-save adder produces two n-bit outputs
  n-bit partial sum bits and n-bit carry bits
All the n bits of a carry-save adder work in parallel
  The carry does not propagate as in a carry-propagate adder
  This is why a carry-save is faster than a carry-propagate adder
Useful when adding multiple numbers (as in multipliers)
Carry-Propagate Adder
+
a0
b0
s0
+
a1
b1
s1
+
a31
b31
s31
. . .
cout
cin
Carry-Save Adder
. . .
+
a31
b31
s'31
c'31
c31
+
a1
b1
s'1
c'1
c1
+
a0
b0
s'0
c'0
c0

## Slide 17: Carry-Save Adders in a Multiplier
ADD the product bits vertically using Carry-Save adders
  Full Adder adds three vertical bits
  Half Adder adds two vertical bits
  Each adder produces a partial sum and a carry
Use Carry-propagate adder for final addition
a0b0
a1b0
a2b0
a3b0
a0b1
a1b1
a2b1
a3b1
a0b2
a1b2
a2b2
a3b2
a0b3
a1b3
a2b3
a3b3
A × B

## Slide 18: Carry-Save Adders in a Multiplier
Step 1: Use carry save adders to add the partial products
  Reduce the partial products to just two numbers
Step 2: Use carry-propagate adder to add last two numbers
P0
FA
a2b0 a1b1
HA
FA
FA
a3b0 a2b1
a0b0
HA
a1b0 a0b1
HA
HA
FA
FA
FA
FA
a3b1 a2b2
FA
a3b2
a2b3
a3b3
a1b3
a0b3
a1b2
a0b2
P1
P2
P3
P4
P5
P6
P7
Carry Save Adder
Carry Propagate Adder
Carry Save

## Slide 19: Summary of a Fast Multiplier
A fast n-bit × n-bit multiplier requires:
  n2 AND gates to produce n2 product bits in parallel
  Many adders to perform additions in parallel
Uses carry-save adders to reduce delays
Higher cost (more chip area) than sequential multiplier
Higher performance (faster) than sequential multiplier

## Slide 20: Next . . .
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 21: Unsigned Division (Paper & Pencil)
= 19 Quotient
Divisor 10112 110110012 = 217 Dividend
-1011
10
101
1010
10100
-1011
1001
10011
-1011
10002 = 8 Remainder
Dividend =
Quotient × Divisor
+ Remainder
217 = 19 × 11 + 8
1
0
0
1
12
Check how big a number can be subtracted, creating a bit of the quotient on each attempt
Binary division is done via shifting and subtraction

## Slide 22: Sequential Division
Uses two registers: HI and LO
Initialize: HI = Remainder = 0 and LO = Dividend
Shift (HI, LO) LEFT by 1 bit (also Shift Quotient LEFT)
  Shift the remainder and dividend registers together LEFT
  Has the same net effect of shifting the divisor RIGHT
Compute: Difference = Remainder – Divisor
If (Difference ≥ 0) then
  Remainder = Difference
  Set Least significant Bit of Quotient
Observation to Reduce Hardware:
  LO register can be also used to store the computed Quotient

## Slide 23: Sequential Division Hardware
Initialize:
  HI = 0, LO = Dividend
Results:
  HI = Remainder
  LO = Quotient
Start
Difference?
2. HI = Remainder = Difference
Set least significant bit of LO
32nd Repetition?
Done
< 0
≥ 0
No
Yes
Shift (HI, LO) Left
Difference = HI – Divisor
shift left
Divisor
32-bit ALU
LO
32 bits
write
sub
32 bits
Difference
sign
set lsb
HI
32 bits
Control

## Slide 24: Unsigned Integer Division Example
Example: 11102 / 01002 (4-bit dividend & divisor)
Result Quotient = 00112 and Remainder = 00102
4-bit registers for Remainder and Divisor (4-bit ALU)
Diff < 0 => Do Nothing
2
0 0 0 0
1 1 1 0
Initialize
0
1
3
4
HI
Difference
LO
Iteration
0 1 0 0
Divisor
< 0
Shift Left, Diff = HI - Divisor
0 0 0 1
1 1 0 0
0 1 0 0
< 0
Shift Left, Diff = HI - Divisor
0 0 1 1
1 0 0 0
0 1 0 0
0 0 1 1
Shift Left, Diff = HI - Divisor
0 1 1 1
0 0 0 0
0 1 0 0
0 0 1 0
Shift Left, Diff = HI - Divisor
0 1 1 0
0 0 1 0
0 1 0 0
HI = Diff, set lsb of LO
0 0 0 1
0 0 1 1
HI = Diff, set lsb of LO
0 0 1 1
0 0 1 0
Diff < 0 => Do Nothing

## Slide 25: Signed Integer Division
Simplest way is to remember the signs
Convert the dividend and divisor to positive
  Obtain the 2's complement if they are negative
Do the unsigned division
Compute the signs of the quotient and remainder
  Quotient sign = Dividend sign XOR Divisor sign
  Remainder sign = Dividend sign
Negate the quotient and remainder if their sign is negative
  Obtain the 2's complement to convert them to negative

## Slide 26: Signed Integer Division Examples
Positive Dividend and Positive Divisor
  Example: +17 / +3 Quotient = +5 Remainder = +2
Positive Dividend and Negative Divisor
  Example: +17 / –3 Quotient = –5 Remainder = +2
Negative Dividend and Positive Divisor
  Example: –17 / +3 Quotient = –5 Remainder = –2
Negative Dividend and Negative Divisor
  Example: –17 / –3 Quotient = +5 Remainder = –2
The following equation must always hold:
Dividend = Quotient × Divisor + Remainder

## Slide 27: Next . . .
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
Integer Division
Integer Multiplication and Division in MIPS

## Slide 28: Integer Multiplication in MIPS
Multiply instructions
  mult Rs, Rt Signed multiplication
  multu Rs, Rt Unsigned multiplication
32-bit multiplication produces a 64-bit Product
Separate pair of 32-bit registers
  HI = high-order 32-bit of product
  LO = low-order 32-bit of product
MIPS also has a special mul instruction
  mul Rd, Rs, Rt Rd = Rs × Rt
  Copy LO into destination register Rd
  Useful when the product is small (32 bits) and HI is not needed
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 29: Integer Division in MIPS
Divide instructions
  div Rs, Rt Signed division
  divu Rs, Rt Unsigned division
Division produces quotient and remainder
Separate pair of 32-bit registers
  HI = 32-bit remainder
  LO = 32-bit quotient
  If divisor is 0 then result is unpredictable
Moving data from HI, LO to MIPS registers
  mfhi Rd (Rd = HI)
  mflo Rd (Rd = LO)
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 30: Integer Multiply and Divide Instructions
Instruction | Meaning | Format |  |  |  |  | 
mult Rs, Rt | HI, LO = Rs ×s Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x18
multu Rs, Rt | HI, LO = Rs ×u Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x19
mul Rd, Rs, Rt | Rd = Rs ×s Rt | 0x1c | Rs | Rt | Rd | 0 | 2
div Rs, Rt | HI, LO = Rs /s Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x1a
divu Rs, Rt | HI, LO = Rs /u Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x1b
mfhi Rd | Rd = HI | Op = 0 | 0 | 0 | Rd | 0 | 0x10
mflo Rd | Rd = LO | Op = 0 | 0 | 0 | Rd | 0 | 0x12
mthi Rs | HI = Rs | Op = 0 | Rs | 0 | 0 | 0 | 0x11
mtlo Rs | LO = Rs | Op = 0 | Rs | 0 | 0 | 0 | 0x13
×s = Signed multiplication, ×u = Unsigned multiplication
/s = Signed division, /u = Unsigned division
NO arithmetic exception can occur

## Slide 31: String to Integer Conversion
Consider the conversion of string "91052" into an integer
How to convert the string into an integer?
Initialize: sum = 0
Load each character of the string into a register
  Check if the character is in the range: '0' to '9'
  Convert the character into a digit in the range: 0 to 9
  Compute: sum = sum * 10 + digit
  Repeat until end of string or a non-digit character is encountered
To convert "91052", initialize sum to 0 then …
  sum = 9, then 91, then 910, then 9105, then 91052
'9'
'1'
'0'
'5'
'2'

## Slide 32: String to Integer Conversion Function
#-----------------------------------------------------------
# str2int: Convert a string of digits into unsigned integer
# Input: $a0 = address of null terminated string
# Output: $v0 = unsigned integer value
#-----------------------------------------------------------
str2int:
li $v0, 0 # Initialize: $v0 = sum = 0
li $t0, 10 # Initialize: $t0 = 10
L1: lb $t1, 0($a0) # load $t1 = str[i]
blt $t1, '0', done # exit loop if ($t1 < '0')
bgt $t1, '9', done # exit loop if ($t1 > '9')
addiu $t1, $t1, -48 # Convert character to digit
mul $v0, $v0, $t0 # $v0 = sum * 10
addu $v0, $v0, $t1 # $v0 = sum * 10 + digit
addiu $a0, $a0, 1 # $a0 = address of next char
j L1 # loop back
done: jr $ra # return to caller

## Slide 33: Integer to String Conversion
Convert an unsigned 32-bit integer into a string
How to obtain the decimal digits of the number?
  Divide the number by 10, Remainder = decimal digit (0 to 9)
  Convert decimal digit into its ASCII representation ('0' to '9')
  Repeat the division until the quotient becomes zero
  Digits are computed backwards from least to most significant
Example: convert 2037 to a string
  Divide 2037/10 quotient = 203 remainder = 7 char = '7'
  Divide 203/10 quotient = 20 remainder = 3 char = '3'
  Divide 20/10 quotient = 2 remainder = 0 char = '0'
  Divide 2/10 quotient = 0 remainder = 2 char = '2'

## Slide 34: Integer to String Conversion Function
#----------------------------------------------------------
# int2str: Converts an unsigned integer into a string
# Input: $a0 = value, $a1 = buffer address (12 bytes)
# Output: $v0 = address of converted string in buffer
#----------------------------------------------------------
int2str:
li $t0, 10 # $t0 = divisor = 10
addiu $v0, $a1, 11 # start at end of buffer
sb $zero, 0($v0) # store a NULL character
L2: divu $a0, $t0 # LO = value/10, HI = value%10
mflo $a0 # $a0 = value/10
mfhi $t1 # $t1 = value%10
addiu $t1, $t1, 48 # convert digit into ASCII
addiu $v0, $v0, -1 # point to previous byte
sb $t1, 0($v0) # store character in memory
bnez $a0, L2 # loop if value is not 0
jr $ra # return to caller