KING FAHD UNIVERSITY OF PETROLEUM AND MINERALS

University Diploma Programs

PHYS 012: Solid State Physics

Preparatory Classroom Building, Building # 7, Room # 116.

QUIZ  #  5

NAME: _____________________________________________   ID: ___________________

====================================================================

Circle the most accurate answer for each of the following questions

Q.1.	The maximum value of collector current in a biased transistor is:

(a)  βDC,	(b)  IC(sat),	(c)  greater than IC(sat),	(d)  IE - IB.

Q.2.	Ideally, a dc load line is a straight line drawn on the collector characteristic curves between:

(a) the Q-point and cutoff,	(b) the Q-point and saturation,    (c) VCE(cutoff) IC(sat),  (d) IC = 0 and IC/ βDC.

Q.3.	If a sinusoidal voltage is applied to the base of a biased npn transistor and the resulting sinusoidal collector voltage is clipped near zero volts, the transistor is:

(a) being driven into saturation,	   (b) being driven into cutoff,	 (c) operating nonlinearly, (d) answers (a) and (c),		   (e) answers (b) and (c).

Q.4.	In a certain voltage-divider biased npn transistor, VB is 2.95 V. The dc emitter voltage is approximately:

(a) 2.25V,	 (b) 2.95V,	   (c) 3.65V,		   (d) 0.7V.

Q.5.	The disadvantage of base bias is that:

(a)  it is very complex,		(b) it produces low gain,		(c) it is too beta dependent,

(d)  it produces high leakage current.

Q.6.	Collector-feedback bias is:

(a) based on the principle of positive feedback,	(b) based on beta multiplication,

(c) based on the principle of negative feedback,	(d) not very stable.

Q.7.	In a voltage-divider biased npn transistor, if the upper voltage-divider resistor (the connected to VCC) opens:

(a) the transistor goes into cutoff,	(b) the transistor goes into saturation,

(c) maximum,	(d) the transistor burns out,	(e) the supply voltage is too high.

Q.8.	In a voltage-divider biased npn transistor, if the lower voltage-divider resistor (the one connected to ground) opens:

(a) the transistor is not affected,	(b) the transistor may be driven into cutoff,

(c) the transistor may be driven into saturation,	(d) the collector current will decrease.

Thursday, 02 January 2003.