KING FAHD UNIVERSITY OF PETROLEUM AND MINERALS

University Diploma Programs

EET 022: Digital Electronics Circuits

Preparatory Classroom Building, Building # 7, Room # 116.

QUIZ  #  1

NAME: _________________________________		        ID: ___________________

=================================================================

Circle the most accurate answer for each of the following questions

Q.1.	The AND operation can be produced with:

(a)   two NAND gates,

(b)   three NAND gates,

(c)   one NOR gate,

(d)   two NOR gates.

Q.2.	All Boolean expressions can be implemented with:

(a)   NAND gates only,

(b)   NOR gates only,

(c)   combinations of NAND and NOR gates,

(d)   combinations of AND, OR gates, and inverters,

(e)    any of these.

Q.3.	A full adder is characterized by:

(a)   two inputs and two outputs,

(b)   three inputs and two outputs,

(c)   two inputs and three outputs,

(d)   two inputs and one output.

Q.4.	The inputs to a full-adder are A = 1, B = 1 and Cin = 0. The outputs are:

(a)   ∑= 1, Cout = 1,

(b)   ∑= 1, Cout = 0,

(c)   ∑= 0, Cout = 1,

(d)   ∑= 0, Cout = 0.

Q.5.	A 4-bit parallel adder can add:

(a)   two 4-bit binary number,

(b)   two 2-bit binary number,

(c)   four bits at a time,

(d)   four bits in sequence.

Friday, 11 October 2002.