KING FAHD UNIVERSITY OF PETROLEUM AND MINERALS

University Diploma Programs

EET 022: Digital Electronics Circuits

Preparatory Classroom Building, Building # 7, Room # 116.

QUIZ  #  4

NAME: _________________________________		        ID: ___________________

=================================================================

Circle the most accurate answer for each of the following questions

Q.1.	Ideally, the accuracy of a 4-bit DAC is:

(a)   approximately 3.1%,

(b)   approximately 0.31%,

(c)   approximately 6.2%,

(d)   approximately 0.62%.

Q.2.	The USB can support up to:

(a)   63 devices,

(b)   14 devices,

(c)   100 devices,

(d)   127 devices.

Q.3.	The RS-232C is:

(a)   a standard interface for parallel data,

(b)   a standard interface for serial data,

(c)   an enhancement of the IEEE 488 interface,

(d)   the same as SCSI.

Q.4.	Most devices are interfaced to a bus with:

(a)   totem-pole outputs,

(b)   tristate drivers,

(c)   pnp transistors,

(d)   resistors.

Q.5.	The type of analog-to-digital converter (ADC) with the fastest conversion time is:

(a)   flash,

(b)   stairstep-ramp,

(c)   tracking,

(d)   simultaneous-conversion.

Wednesday, 01 January 2003.