KING FAHD UNIVERSITY OF PETROLEUM AND MINERALS

ELECTRICAL ENGINEERING DEPARTMENT

SECOND SEMESTER 2005/2006

EE 201 FINAL EXAM

LOCATION: 11-133

TIME: 12:30 PM

DATE: MONDAY, 29-5-2006

Student’s Name:  ………………………………………….

Student’s I.D. Number:   ………………….

Section Number: …………………

| PROBLEM 1 |  |
| --- | --- |
| PROBLEM 2 |  |
| PROBLEM 3 |  |
| PROBLEM 4 |  |
| PROBLEM 5 |  |
| TOTAL |  |

Problem 1

As indicated in the given circuit, the currents through the  and the  resistors are  and , respectively. Calculate:

a) The value of the supply voltage .

b) The value of the unknown resistance .

c) The power absorbed by the  source. (Indicate if this power is actually absorbed or actually delivered).

d) The power absorbed by . (Indicate if this power is actually absorbed or actually delivered).

|  | Answer: a) b) c) (Actually absorbed) (Actually delivered) d) (Actually absorbed) (Actually delivered) |
| --- | --- |

Problem 2

In the circuit shown:

a) Find the Thevenin's equivalent circuit seen between the terminals "a" and "b".

b) A load resistor  is to be connected between "a" and "b". Calculate the value of  for maximum power transfer.

c) Calculate the maximum power transfer to .

|  | Answer: a) b) c) |
| --- | --- |

Problem 3

In the circuit shown, the switch remains in position (1) for a long time. It is suddenly moved to position (2) at . Find:

a)  for       and       for .

b)  for      and       for .

|  | Answer: a) b) |
| --- | --- |

Problem 4

For the circuit shown, find the steady-state current .

[Hint: Use superposition].

|  | Answer: |
| --- | --- |

Problem 5

a) As shown in the given circuit, loads A and B are connected series. Load A absorbs 9KW at a power factor of 0.60 (leading). The complex power absorbed by circuit B is given by . The source frequency .

Use the given information to calculate the phasor current  in rms units.

|  | Answer: |
| --- | --- |

b) In the circuit shown below, load A consumes 5.9 KW at a power factor of 0.70 (lagging). A capacitance  is connected in parallel with load A, so that the combined load has a unity power factor. The source frequency .

Calculate the value of in Farad.

|  | Answer: |
| --- | --- |