KING FAHD UNIVERSITY OF PETROLEUM AND MINERALS

ELECTRICAL ENGINEERING DEPARTMENT

COURSE			EE # 340

SECTION			ALL

EXAM			FINAL

PLACE			7/121(3,4),122(2) and 124(1)

DATE			June 3, 2006

TIME			7:00 P.M.

INSTRUCTORS		Drs: E. Hassan, H. Jamid and H. Ragheb

________________________________________________________________________

STUDENT NAME	--------------------------

STUDENT   I.D.		---------------------------

Student Lab.  		---------------------------

ATTEMPT ALL FIVE QUESTIONS

| PROBLEM 1 |  |
| --- | --- |
| PROBLEM 2 |  |
| PROBLEM 3 |  |
| PROBLEM 4 |  |
| PROBLEM 5 |  |
| TOTAL |  |

Q1-(a)- In the configuration shown, Region 1 is defined			Region 2

by  0≤ ρ ≤ a and region 2 is defined by a≤ ρ ≤ ∞

Given that:

and ,  	Find:

i- 	in region 2 at the boundary : 	ρ = a.

ii- Find Vpq where p(a/4,30o,5) and q(3a/4,60o,10).

Q1-(b)-   A vertical plane (perpendicular to the z=0 plane) and intersects the z=0 plane at the line 2y+x=4, is charged with surface charge density ρs = 4 C/m2 . Find the electric field at the origin.

Q2-   The diagram below shows an infinitely long filamentary wire, which carries the sinusoidal current:

The rectangular loop of dimensions  shown in the diagram lies entirely in the  plane. This loop moves away from the filamentary wire with the constant velocity .  At , the left hand side of the rectangular loop is located at a distance  from the filamentary wire. Assume the medium is air.

Derive an expression for the EMF induced in the rectangular loop for .

Q-3   The diagram below shows an infinitely long filamentary wire that passes through the center of an  toroidal coil having a rectangular cross-sectional area. The core of the toroidal coil has a relative permeability . The inner and outer radii of the coil are  and , respectively. As seen in the diagram, the filamentary wire carries D.C. current and no current flows in the toroidal coil.

a) Derive an expression for the magnetic flux through one turn of the toroidal coil.

b) Derive an expression for the mutual inductance between the filamentary wire and the toroidal coil.

c) Using the following set of values: , , , , ,  and , calculate:

i) The mutual inductance in Henry.

ii) The magnetostatic energy stored in the core of the toroidal coil (Hint:  and also ).

Q-4- A lossy non-magnetic dielectric has an intrinsic impedance  at  rad/sec. If a plane wave is propagating through this medium having a magnetic field given by

Find:

- the electric field ,

- the attenuation constant  and the skin depth ,

- the relative permittivity ,

- the conductivity .

- The phase velocity.

Q-5- A uniform plane wave in free space ( ) with the electric field component,

V/m

hits normally a dielectric surface at as shown below. Assuming that the dielectric surface is smooth and ,  and , determine

- The wavelength of the wave in air.

- Calculate the reflection and transmission coefficients.

- Write expressions for the total electric and magnetic fields in mediums 1 & 2.

- Calculate the average reflected power over a rectangular area of  m2 inclined by an angle 60 with respect to z-axis as shown.

Gauss’s law :

,       ,      ,      ,

E Field of infinite line and infinite plane:

Boundary conditions: 		        F/m

Biot-Savart law :   ,   Ampere’s Law     H/m

H Field of infinite line and infinite plane:  ,,

Boundary conditions:     ,     , mutual inductance

Faraday’s law   :

phase velocity:    ,

,     ,

,       ,

For good conductor :    ,     ,

For good Dielectric:   ,    ,

Reflection and Refraction: For  normal incidence take all angles to be ZEROS.

,      ,

,    ,        ,

# Text boxes

a

Region 1

32 m2  rectangular plane