Course :       EE 340

Instructor : Dr. H. Ragheb

Examination:    Second Exam

Date   :          Jan.  5, 2008

Section :                2 and 3

Time :           8:00-9:30 PM

| Student Name: |  |
| --- | --- |
| Student Number: |  |

| Problem 1 |  |
| --- | --- |
| Problem 2 |  |
| Problem 3 |  |
| Total |  |

Answer  all  Questions.

Problem (1)  [12 points]

A capacitor consists of two concentric conducting spheres of radii a and b where b>a. The dielectric material between the conducting surfaces has a relative permittivity  where  is measured from the center. Determine the capacitance of the capacitor..

Problem (2-a)  [12 points]

The filamentary current loop shown in Fig 2-a consists of line segments and semi-circles whose centers are at the origin. Determine the magnetic field intensity at the origin in terms of  a , b , and I.

Fig. 2-a.

Problem (2-b)  [12 points]

Consider an infinitely long conducting cylinder of radius a which carry a uniform current density. A coaxial cylindrical surface of radius b () carrying a uniformly distributed current sheet of .

- Find the magnetic field everywhere.

- Find the ratio between  and which results in zero magnetic field for .

Fig. 2-b

Problem (3)  [9 points]

A current sheet of  kA/m separates two regions at . Region 2, , has a magnetic field intensity  kA/m and a relative permeability of 200. If  region 1, , has a relative permeability of 1000, determine the magnetic field intensity in this region.

# Text boxes

b

a