King Fahd University of Petroleum & Minerals

Electrical Engineering Department

# EE-390; Exam 2,  (Time : 1 hour)

| Prob.1 | Prob.2 | Prob.3 | Total |
| --- | --- | --- | --- |

Name : I.D.

1.  For the isolated I/O circuit in the figure below, on chip 6, Port A is used as an input port, Port C & Port B are used as output ports. If the 8255A chips are working in Mode 0, assume the don’t care address pins are at ‘logic 0’ level to;

- Find the addresses of ports A, B, C and the control register in HEX

- Write a program segment (do not include Title, Stack etc.), with maximum 9 lines of code, that will input data using port A, invert the inputted data and output them to both port B and port C

2. The figure below is a 64 line parallel output circuit of a 8088 microcomputer, find the addresses of PORT 2 and PORT 7 .

(Assume  don’t care address pins are at ‘logic 1’ level)

Address of port 2________________________H

Address of port 7________________________H

- In executing the instruction		OUT DX, AL

The 8088 processor performs a bus operation. Complete the timing diagram showing: Logic levels at the specified pins. (Assume minimum-mode, AX=12BAH, DS=0B1DCH, IF=1, and DX=031AH).

T1	                T2		  T3	        T4

CLK

AD3

AD2

AD1

AD0

ALE

IO/M’

WR’

RD’

MN/MX’

A19/S6

A18/S5

A17/S4

# Text boxes

C

B

A

CE

D0 – D7

82C55A

G1

Control  bus

Address bus A0 – A15

Data bus D0 – D7

Port B

Port C

0

2

4

6

8

10

12

14

Port A

74F138

p7

p1

p0