King Fahd University of Petroleum & Minerals

###### Electrical Engineering Department

# EE203: Electronics I

# Project (5%)

(Due 18th of December)

Objectives:

- To design Amplifier circuit to meet certain specifications.

Tasks:

It is requested to design an audio amplifier which will be inserted between a TV receiver and a stereo system. The designed voltage amplifier should exhibit the following specification:

- - Small signal overall voltage gain >50 V/V.

- - Input resistance Ri > 40kΩ.

- - Output resistance Ro < 1kΩ.

Given that:

- Load resistance RL= 1kΩ.

- Single supply voltage of VCC= 12 V.

- Input voltage (vsig) and the internal resistance Rsig

vsig =0.01 sin(2π 1000t) and Rsig = 2kΩ.

- Check transistors' mode of operation.

(Use transient analysis to verify your hand calculation)

Include in your report:

- Detailed theoretical design and calculations ( put justifications for assumptions and avoid trail and error approach)

- Spice schematic or netlist for the designed amplifier

- Use SPICE to plot vo(t) and verify your design.

- Compare theoretical and simulated results (voltage gain).

Notice:

There will be an oral exam during class time on Monday 23rd December.