Home Work # 2

Design the MOSFET voltage amplifier shown below.

- Small signal gain >30.

- Verify the computed nodal voltages, currents (for small signal & DC) and gain of the designed amplifier with the results obtained form the related PSPICE program.

- Use 0.5um CMOS technology (CMOS parameters can be obtained from Sedra’s book 4th edition appendix D.5).

Load resistance RL= 10kΩ.

Single supply voltage of VCC= 6 V.

- Plot the voltage gain vo for the input voltage vi =0.01 sin (62800t).

- Use AC analysis to find frequency bandwidth of the amplifier.

- Calculate Ri & Ro.