### Fully Differential Second-Order Filter

### S. M. Al-Shahrani

Department of Electrical Engineering, King Fahd University of Petroleum and Minerals, Box 185, Dhahran 31261, Saudi Arabia   saadms@kfupm.edu.sa

### Abstract

In this paper a new fully-differential lowpass/ bandpass second-order filter is proposed. The proposed filter uses three fully-differential Second-generation Current-conveyors (FDCCII), four resistors and two capacitors, doesn’t require any matching condition and enjoys independent tuning of the gain and the parameters ωo, and ωo/Q.  Experimental results are included.

### I. Introduction

At present there is a growing interest in designing fully differential analog filters [1-2].  This is attributed to the resulting improvement in power supply noise rejection, dynamic range and harmonic distortion.  Traditionally, a fully differential analog filter can be realized using two identical single ended filters.  However, this requires matching of the active and passive components used in both filters.

Recently fully differential filters are realized using single differential active components instead of two single ended one [1-2]. In [1] a fully differential Sallen-Key filter is presented.  It uses a differential amplifier and eight passive components and requires four matching conditions.  Because of the use of unity gain negative feedback structure, matching condition in the active component is not a critical issue, especially with high open loop gain amplifier.  A second-order lowpass filter based on a single fully differential current conveyor is proposed in [2].  This circuit requires the current gain between the x and z terminals of the current conveyors to be matched.  It uses ten passive components and requires five matching conditions.  The gain of this filter can be controlled via grounded capacitors.  Both filters reported in [1] and [2] enjoy orthogonal tuning of the parameters ωo, and ωo/Q.

In this paper, a new fully differential filter that does not require any matching condition is presented.  The proposed circuit uses the fully differential current conveyor and enjoys the following advantages:

- it uses only two capacitors and four resistors;

- there is no matching condition requirement between components.

- it enjoys independent tuning through resistors for ωo, ωo/Q, and the gain;

- it has large input impedance therefore can be cascaded;

- it realizes lowpass and bandpass filters.

### II. Circuit Description

The circuit symbol of the fully differential current conveyor (FDCCII) is shown in Fig. 1a [3]. FDCCII can be realized using two current sensed op-amps [3].  Its characteristic can be modeled as

and	Vy1 - Vx1 = Vy2 - Vx2	(1)

The proposed circuit is shown in Fig. 1b.  The lowpass filter transfer function can be expressed as

(2)

and the bandpass filter transfer function as

(3)

From (2), the parameters ωo, ωo/Q, and Q can be expressed as

(4)

(5)

(6)

From (2)-(5) one can see that the lowpass gain, the gain of the bandpass at the center frequency, and the parameters ωo, and ωo/Q can be controlled independently through G1, G2, and G5 respectively.

The source of non-ideality in the FDCCII is deviation of the voltage gain between x and y terminals and the current gain between the x and z terminals from unity.  The former source of error is not a critical one because of the unity negative feedback used inside the FDCCII, which forces terminal x and y to have equal voltages.  Taking into account the non-ideality of the FDCCII, namely, izi= αixi, i=1, 2, 3 where α = 1-ε and ε (<<1) denotes the current tracking error of a FDCCII, (2) becomes

(7)

From (7), the parameters ωo, ωo/Q, and Q can be expressed as

(8)

(9)

(10)

From equations (7)-(9), it is clear that the current-tracking errors will not change the transfer function of the filter.  It will affect the quality factor (Q), center frequency (ωo), and gain values.

Using the standard definition of sensitivity, the active and passive sensitivits of the proposed filter can be expressed as

-

.

Thus, the proposed filter enjoys low active and passive sensitivities.

# III. Experimental Results

To verify the theoretical prediction of the proposed circuit, it has been realized using discrete components. The proposed circuit of Fig. 1(b) was built using C4=C5=5nF, R2=2KΩ, R3=3KΩ, R5=2.5KΩ (for LPF), and R5=10KΩ (for BPF).  Rather than realizing the FDCCII using two opamps as reported in [3], the experimental result reported here were obtained using plus-type second-generation two current-conveyors (AD844) [4].  Figures 2 and 3 show the experimental results obtained from the proposed circuit.  Figures 2 and 3 also show the theoretical transfer characteristic of the proposed filter.  From Figures 2 and 3 it appears that the measured and calculated results are in close agreements.

### IV. Conclusion

Using three FDCCIIs, four resistors and two capacitors a new circuit for realizing fully-differential lowpass/bandpass second-order filter has been presented.  The proposed circuit enjoys independent tuning of the gain, and the parameters ωo, and ωo/Q of the filters, does not require any matching conditions and enjoys low active and passive sensitivities.  The experimental results are generally in excellent agreement with the proposed theory. The discrepancies between measured and calculated results are attributed to the nonidealities of the current-conveyors used to implement the FDCCIIs.  It worth mentioning that all of the current mirrors used in the proposed circuit are included in feedback loops and this will reduce the harmonic distortion [5].

Acknowledgment: The author would like to thank Dr. M. T.  Abuelma’atti for his valuable comments.  Acknowledgment is also due to King Fahd University of Petroleum and Minerals for supporting the work.

#### References

[1]	Shi, C., Wu, Y., Elwan, H., and ISMAIL, M., 2000, “A Low-power high-linearity CMOS baseband filter for wideband CDMA applications,” ISCAS, 36, pp. 152-154.

[2]	Alzaher, H., Elwan, H., and ISMAIL, M., 2000, CMOS baseband for WCDMA integrated wireless receivers. Electron. Lett., 36, pp. 1515-1516.

[3]	Alzaher, H., Elwan, H., and ISMAIL, M., 2000, CMOS fully differential second-generation current conveyor. Electron. Lett., 36, pp. 1095-1096.

[4]	Analog Devices., 1990, Linear Products Data Book. Norwood, MA: Artech House.

[5]	Bruun, Erick., 1998, Harmonic Distortion in CMOS Current Mirrors. ISCAS, 1, pp. 567 –570.

# Text boxes

y1

y2

FDCCII

x1

x2

z1

z2

z1

x1

y2

z2

z1

x2

y1

z2

z1

x2

y1

x1

y2

z2

Figure 2: Comparisons between the theoretical and

experimental results for the lowpass filter.

R3

R5

x2

y1

x1

y2

C4

R1

R2

C5

+

Vi

-

+

Vo2

-

+

Vo1

-

R1  (Ω)

580

1K

FDCCII-2

FDCCII-3

FDCCII-1

(b)

(a)

Figure1: a) Block Diagram of FDCCII

b) Proposed FDCCII based Fully-Differential Filter FilterSallen-Key Filter

Figure 3: Comparisons between the theoretical and experimental results for the bandpass filter.

R1  (Ω)

1k

2K