The Study of Systems

System: It is a medium that relates a cause to an effect, or an input to an output

The study and design of physical systems often consists of:

- Performance specifications

- Modeling

- Simulations

- Analysis

- Optimization

- Physical Realization

Modeling is the representation of a system and all its components in a mathematical form.

Depending on the questions asked, or depending on the operating ranges, a physical system may have different models

Example: An Automobile may be modeled as a single particle if we are studying traffic flow but may be modeled as a spring-mass-damper system if we are interested in the vibration of the occupants

Once a model is selected for a physical system, the next step is to develop mathematical equations to describe the system from the fundamental physical principles such as:

- Newton’s law for mechanical systems

- Kirchhoff’s voltage and current laws in electrical systems

- Laws of thermodynamics and transport phenomena in fluid and thermal systems

After the mathematical equations for the model have been obtained the next step in the study of systems involves both

- Quantitative

  - System responses to specified inputs

- Qualitative

  - Stability

  - Controllability

  - Observability

If the response of the system is found to be unsatisfactory then an engineering design phase termed improvement or optimization is initiated

In some cases a system parameter may be adjusted to improve the response but in other cases compensation devices must be injected into the system

Finally in the realization phase the proposed system must be built using actual physical hardware

System Classification

#### Systems models are classified by their types of describing equations

System Classes

# Distributed 			Lumped

Parameter 			Parameter

Stochastic			Deterministic

Continuous				Discrete

Time					Time

## Nonlinear				Linear	Nonlinear		Linear

### Time 					Time

Varying					Invariant