HW

4

- Consider the following two state-space descriptions:

and

Are the two state-space equations equivalent? If not, show why not. If so, prove your answer.

- Problem 5.1 of Text

- Problem 5.4 of Text

- Problem 5.7 of Text

- Is the discrete-time homogenous state equation

marginally stable? Asymptotically stable?