BIT MANIPULATION INSTRUCTIONS

LOGIC INSTRUCTIONS	           SHIFT INSTRUCTIONS	                  ROTATE INSTRUCTIONS

AND , OR , XOR , NOT , TEST,						    ROL , ROR , RCL , RCR

BT, BTC, BTR, BTS																																								LOGICAL SHIFTS		 ARITHMETIC SHIFTS						              SHL , SHR, SHRD, SHLD		 SAL , SAR

# LOGIC INSTRUCTIONS

All logic instructions are binary except NOT which is unary. The syntax of the instructions is:

AND  Destination , Source

OR     Destination , Source

XOR  Destination , Source

TEST Destination , Source

NOT  Destination

- The result of the operation is stored in the Destination, which must be a register or a memory location.

- The Source may be a constant, register, or memory location.

- The Destination and Source cannot both be memory locations.

- The Destination and Source must be of the same size.

All logic instructions, except TEST, may modify the Destination operand. The TEST instruction does not modify any of its operands; however it affects the flags similar to the AND instruction.

All logic instructions, except NOT, affect the flags: If the result in the Destination is zero, the Zero flag is set, otherwise it is cleared. The Carry- and Overflow- flags are always cleared. NOT does not affect any flag.

A logic instruction operates on each corresponding Destination-Source bit pair. The truth tables for logic instructions are:

| Bit1 Bit2 | Bit1 AND Bit2 | Bit1 TEST Bit2 | Bit1 OR Bit2 | Bit1 XOR Bit2 |
| --- | --- | --- | --- | --- |
| 0 1 0 1 1 | 0 0 0 1 | 0 0 0 1 | 0 1 1 1 | 0 1 1 0 |

| Bit | NOT Bit |
| --- | --- |
| 0 1 | 1 0 |

Example:

MOV  BL ,  01010111B

AND  BL ,  11110000B

____________________________

Result in BL :	     01010000B

# Setting, clearing and inverting selected bits in the Destination operand

One use of AND, OR, and XOR is to modify selected bits in the Destination operand. To do this, a Source bit pattern known as a mask is constructed. The mask bits are chosen so that the selected bits are modified in the desired manner when an instruction of the form:

LOGIC_INSTRUCTION    Destination , Mask

is executed. The Mask bits are chosen based on the following properties of AND, OR, and XOR :

If X represents a bit (0 or 1) then:

X   AND   0  =  0			X   OR  0   =  X				X   XOR  0  =  X

X   AND   1  =  X			X   OR   1  =   1				X    XOR  1  =   X

Thus:

- The AND instruction can be used to clear specific Destination bits while preserving the others. A zero mask bit clears the corresponding Destination bit; a one mask bit preserves the corresponding destination bit.

Example:		XXXXXXXXB	Destination

AND	00101011B   Mask

00X0X0XXB

- The OR instruction can be used to set specific Destination bits while preserving the others. A one mask bit sets the corresponding Destination bit; a zero mask bit preserves the corresponding Destination bit.

Example:		XXXXXXXXB	Destination

OR	11101001B   Mask

111X1XX1B

- The XOR instruction can be used to invert specific Destination bits while preserving the others. A one mask bit inverts the corresponding Destination bit; a zero mask bit preserves the corresponding Destination bit.

Example:			XXXXXXXXB	  Destination

XOR	10000101B   Mask

XXXXXXXXB

Examples:

- The instruction

AND  BL , 11110000B

clears the 4 low-order bits of BL while leaving the 4 high-order bits unchanged.

- The instruction

OR  AX , 1100000000000000B

Sets bits 15 and 14 of AX while leaving other bits unchanged.

- The instruction

XOR  CL , 00001010B

Inverts bits 1 and 3 of CL while preserving the others.

- Write instructions to make the high 3 bits of CL equal to the high 3 bits of AL and the low 5 bits of CL equal to the low 5 bits of BL, i.e., CL should have the bit pattern:

| a7 | a6 | a5 | b4 | b3 | b2 | b1 | b0 |
| --- | --- | --- | --- | --- | --- | --- | --- |

Solution:

PUSH  BX

MOV  CL  ,  AL

AND  CL  ,  11100000B

AND  BL  ,  00011111B

OR  CL  ,  BL

POP  BX

## Changing a letter to its opposite case

- Suppose CL contains a lowercase alphabetic letter. To change that letter to uppercase, we subtract 20H from CL:

SUB  CL , 20H

- Suppose BL contains an uppercase alphabetic letter. To change that letter to lowercase, we add 20H to BL:

ADD  BL , 20H

- For any alphabetic letter, bit 5 of its ASCII code is 1; but for the corresponding uppercase letter bit 5 is 0. The remaining bits are similar:

| Letter ASCII code | Letter ASCII code |
| --- | --- |
| ‘a’ 0110 0001B ‘b’ 0110 0010B ‘c’ 0110 0011B . . . ‘y’ 0111 1001B ‘z’ 0111 1010B | ‘A’ 0100 0001B ‘B’ 0100 0010B ‘C’ 0100 0011B . . . ‘Y’ 0101 1001B ‘Z’ 0101 1010B |

Thus a lowercase alphabetic letter can also be converted to uppercase by clearing bit 5 of its ASCII code. This can be done by using an AND instruction with the mask 11011111B or 0DFh. Example:

MOV  DL , ‘j’

AND  DL , 11011111B

An uppercase alphabetic letter can also be converted to lowercase by setting bit 5 of its ASCII code. This can be done by using an OR instruction with the mask 00100000B or 20H. Example:

MOV  AL  ,  ‘M’

OR  AL , 00100000B

To convert a lowercase or uppercase letter to its opposite case we need only invert bit 5 of its ASCII code. This can be done by using an XOR instruction with the mask 00100000B.

# Converting an ASCII digit to a Decimal digit and vice versa

An ASCII digit (‘0’, ‘1’, ‘2’, ‘3’, ‘4’, ‘5’, ‘6’, ‘7’, ‘8’, or ‘9’) has an ASCII code which is 30H more than the corresponding Decimal digit. Thus one way of converting an ASCII digit to the corresponding Decimal digit we subtract 30H from the ASCII digit. Example:

MOV  DH  ,  ‘4’

SUB  DH  ,  30H

Similarly one way of converting a Decimal digit to the corresponding ASCII digit is to ADD 30H to the Decimal digit. Example:

MOV  CL  ,  8

ADD  CL  ,  30H

However, if we compare the ASCII codes of corresponding ASCII- and Decimal-digits:

| Decimal digit ASCII code | ASCII digit ASCII code |
| --- | --- |
| 0 0000 0000B 1 0000 0001B 2 0000 0010B . . . 8 0000 1000B 9 0000 1001B | ‘0’ 0011 0000B ‘1’ 0011 0001B ‘2’ 0011 0010B . . . ‘8’ 0011 1000B ‘9’ 0011 1001B |

We see that bits 5 and 6 of a Decimal digit are both 0, whereas bits 5 and 6 of the corresponding ASCII digit are both 1. The remaining bits are similar. Thus another way of converting an ASCII digit to the corresponding Decimal digit is to use the AND instruction with the mask 00001111B (i.e. 0FH) or with the mask 11001111B (i.e. 0CFH) to clear bits 5 and 6 of the ASCII digit. Example:

MOV  BH  ,  ‘3’

AND  BH  ,  0FH

Similarly, another way of converting a Decimal digit to the corresponding ASCII digit is to use the OR instruction with the mask 00110000B (i.e. 30H) to set bits 5 and 6 of the Decimal digit. Example:

MOV  CH  ,  6

OR  CH  ,  00110000B

# Examining selected bits in the Destination Operand

The Logic Instructions can be used to examine the status of selected bits in the destination operand. Examples:

- Check if bit 2 of AL is set or clear:

.   .   .

PUSH  AX

AND  AL  ,  00000100B

POP  AX

JZ  BIT_IS_CLEAR

.

.	; action if bit 2 is set

.

JMP  DONE

BIT_IS_CLEAR:

.

.	; action if bit 2 is clear

.

DONE:

Note: This example can be solved using the TEST instruction:

TEST  AL  ,  00000100B

JZ  BIT_IS_CLEAR

.

.	; action if bit 2 is set

.

JMP  DONE

BIT_IS_CLEAR:

.

.	; action if bit 2 is clear

.

DONE:

- Check whether bits 0, 2, 4 and 5 of DL are all clear:

TEST  DL  ,  00110101B

JZ    ALL_4_BITS_CLEAR

.

.	; action if any of bits 0, 2, 4, and 5 is set

.

JMP  DONE

ALL_4_BITS_CLEAR:

.

.	; action if  each of bits 0, 2, 4, and 5 is clear

.

DONE:

- Check if any of bits 0, 2, 4 and 5 of DL is clear:

PUSH  DX

OR     DL  ,  11001010B

CMP  DL  ,  11111111B

POP   DX

JNE  AT_LEAST_ONE_BIT_CLEAR

.

.

.

JMP  DONE

AT_LEAST_ONE_BIT_CLEAR:

.

.

.

DONE:

- Check if each of bits 5, 3, and 1 of CL are set:

PUSH  CX

AND  CL  ,  00101010B

CMP  CL  ,  00101010B

POP  CX

JE  ALL_3_BITS_SET

.

.	; action if any of bits 5, 3, and 1 is not set

.

JMP  DONE

ALL_3_BITS_SET:

.

.	; action if each of bits 5, 3, and 1 is set

.

DONE:

Note: This example can also be solved using the OR instruction:

PUSH  CX

OR  CL  ,     11010101B

CMP  CL  ,  11111111B

POP  CX

JE  ALL_3_BITS_SET

.

.	; action if any of bits 5, 3, and 1 is not set

.

JMP  DONE

ALL_3_BITS_SET:

.

.	; action if each of bits 5, 3, and 1 is set

.

DONE:

- INT 16H, function 02H can be used to examine the keyboard flags at the BIOS data area, at the Segment: Offset address 0000:0417h. The function returns in the AL register the keyboard flags. If a flag is set to 1 then it indicates that a particular control key has been pressed as shown below:

| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |

Insert on     	               		          				Right shift key down

Caps Lock on								Left shift key down

Num Lock on								Ctrl key down        	Scroll Lock on								Alt key down

If the fragment below is executed, a jump to label L1 is taken if the Alt-Ctrl-Right shift key combination has been pressed:

MOV  AH , 02H

INT  16H

AND  AL  ,  00001101B

CMP  AL  ,  00001101B

JE  L1

JMP  L2

L1:

.

.

.

L2:

- Determine if any of the four lowest bits of  SI contains a 1:

TEST  SI  ,  000FH

JNZ  TRUE

.

.

.

JMP  DONE

TRUE:

.

.

.

DONE:

- Check whether a 16-bit memory operand NUM contains an even or an odd number:

(Note: An even number contains a 0 in bit 0; whereas an odd number contains a 1)

TEST  NUM  ,  0001H

JZ  EVEN_NUMBER

.

.

.

JMP  DONE

EVEN_NUMBER:

.

.

.

DONE:

- Determine if bits 5, 4, and 3 of AL contain 101 :

PUSH  AX

AND  AL  ,  00111000B

CMP  AL  ,  00101000B

POP  AX

JE  TRUE

.

.

.

JMP  DONE

TRUE:

.

.

.

DONE:

- Determine whether both AL and BH are zero:

PUSH  AX

OR  AL  ,  BH

POP  AX

JZ  TRUE

.

.

.

JMP  DONE

TRUE:

.

.

.

DONE:

- Determine whether bits 7 and 6 of BL have the same state as bits 7 and 6 of AL :

PUSH  BX

XOR  BL  ,  AL

AND  BL  ,  11000000B

POP  BX

JZ   SAME_STATE

.

.

.

JMP  DONE

SAME_STATE:

.

.

.

DONE:

- Let bi denote bit i of BL. Modify  BL such that:

1	if  b0 = b1 = b2

(

b3  =   (

(

- Otherwise

leave the other bits of BL unchanged.

TEST  BL  ,  00000111B

JZ  SETBIT3			; Jump if bits 0, 1, and 3 are all clear

PUSH  BX

AND  BL  ,  00000111B

CMP  BL  ,  00000111B

POP  BX

JE  SETBIT3			; Jump if bits 0, 1, and 3 are all set

AND  BL  ,  11110111B		; Clear bit 3 while preserving the rest

JMP  DONE

SETBIT3:	OR  BL  ,  00001000B		; Set bit 3 while preserving the others

DONE:

### Clearing a general-purpose register operand or a memory operand to zero

A register operand can be cleared to zero using any of the instructions: MOV, SUB, AND, and XOR. Examples:

MOV  BL  , 0

SUB  AX  ,  AX

AND  CL  ,  0

XOR  DH  ,  DH

A memory operand can be cleared to zero using either the MOV or AND instruction. Examples:

MOV  VAR1 ,  0

AND  ARRAY[2]  ,  0

# The NOT and NEG instructions

The NOT instruction, whose syntax is:

NOT  Destination

is a logical instruction which inverts all the bits of a register or memory operand, i.e., it forms the 1’s complement of the operand. The NEG (NEGate) instruction, whose syntax is:

NEG  Destination

is an arithmetic instruction which forms the 2’s complement (i.e., 1’s complement + 1) of an operand.

#### BIT test instructions

The 80386 and higher 8086 processors contain additional test instructions that test bit positions. These instructions do not accept byte operands:

| Instruction | Operands | Comment |
| --- | --- | --- |
| BT | r/m16 , r16 r/m 16 , imm8 r/m 32 , r32 r/m 32 , imm8 | BT (Bit Test) tests the destination bit specified by the source and places the value of the bit in the Carry flag. |
| BTC |  | BTC (Bit Test and Complement) tests the destination bit specified by the source, it copies that bit to the Carry flag, and complements (i.e., inverts) the original bit in the destination. |
| BTR |  | BTR (Bit Test and Reset) tests the destination bit specified by the source, copies that bit to the Carry flag, it then clears the original bit in the destination. |
| BTS |  | BTS (Bit Test and Set) tests the destination bit specified by the source, copies that bit to the Carry flag, it then sets the original bit in the destination. |

Examples:

- BT  AX ,  4

JC  L2		; Jump if bit 4 of AX is set

.   .   .

L2: .   .   .

- MOVZX   EAX,  BYTE  PTR  DS:[04A2H]		; copy memory byte into 32-bit register

BTC  EAX, 2					; test and compliment bit number 2

MOV  DS:[04A2H],  AL				; write modified byte back to memory

JC   bit2set					; branch if original bit number 2 was set

(c)	BTR	MY_FLAG, 7	; Clear the high-order bit of byte MY_FLAG

JNC   NOT_SET		; branch if the original bit was clear

##### OTHER INSTRUCTIONS THAT MANIPULATE BITS

- BSF (Bit Scan Forward), and BSR (Bit Scan Reverse) instructions

These instructions are available in 80386 and higher Intel processors:

| Instruction | Operands |
| --- | --- |
| BSF | r16 , r/m 16 r32 , r/m 32 |
| BSR |  |

BSF scans a source word or double-word for a one-bit, from the rightmost bit towards the leftmost bit. If a one-bit is found, the bit position of this rightmost one-bit is stored in the destination register, and the Zero Flag (ZF) is cleared. If the source is zero, the Zero Flag is set, and the value of the destination register is undefined.

BSR scans a source word or double-word for a one-bit, from the leftmost bit towards the rightmost bit. If a one-bit is found, the bit position of this leftmost one-bit is stored in the destination register, and the Zero Flag (ZF) is cleared. If the source is zero, the Zero Flag is set, and the value of the destination register is undefined.

Examples:

- MOV  EAX,  60000000H

BSF  EBX,  EAX		; EBX ( 29	,  ZF ( 0

- MOV  ECX,   TABLESIZE –1		; index of last entry in double-word TABLE

L1:   BSR  EAX,  TABLE[ECX*4]		; scan for non-zero bit

JNZ  FOUND_ONE_BIT

LOOP  L1

NO_ONE_BIT_FOUND:

.

.

.

JMP  DONE

FOUND_ONE_BIT:

.

.

.

DONE:

- LAHF (Load AH with Flags) and SAHF (Store AH in FLAGS/EFLAGS)

LAHF copies the low-order byte of the FLAGS register or the EFLAGS register into the AH register. It thus copies SF, ZF, AF, PF, and CF to AH bits 7, 6, 4, 2, and 0, respectively. The contents of the remaining bits (5, 3, and 1) are undefined.

| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SF | ZF |  | AF |  | PF |  | CF |

Fig: Low-order byte of the FLAGS or EFLAGS register

SAHF copies the contents of the AH register into bits 7, 6, 4, 2, and 0 of the FLAGS or the EFLAGS register.