Suggested problems

Chapter 25

The quiz questions will be same or very similar to the following text-book problems.  Refer to the course website for the latest version of this document.  You are encouraged to seek the help of your instructor during his office hours.

2. The capacitor in Fig. 25-25 has a capacitance of 25 μF and is initially uncharged. The battery provides a potential difference of 120 V. After switch S is closed, how much charge will pass through it?

Answer:  3.0×10−3 C = 3.0 mC

4. The plates of a spherical capacitor have radii 38.0 mm and 40.0 mm. (a) Calculate the capacitance. (b) What must be the plate area of a parallel-plate capacitor with the same plate separation and capacitance?

Answer:  (a) 8.45×10−11 F = 84.5 pF ;  (b) 19.1×10−3 m2 = 191 cm2

14. In Fig. 25-30, the battery has a potential difference of V = 10.0 V and the five capacitors each have a capacitance of 10.0 μF. What is the charge on (a) capacitor 1 and (b) capacitor 2?

Answer:  (a) 1.00×10−4 C = 100 µC ;  (b) 2.00×10−5 C = 20.0 µC

28. Figure 25-43 displays a 12.0 V battery and 3 uncharged capacitors of capacitances 𝐶1= 4.00 𝜇𝐹, 𝐶2= 6.00 𝜇𝐹, and 𝐶3= 3.00 𝜇𝐹. The switch is thrown to the left side until capacitor 1 is fully charged. Then the switch is thrown to the right. What is the final charge on (a) capacitor 1, (b) capacitor 2, and (c) capacitor 3?

Answer:  (a) 32.0 µC ;  (b) 16.0 µC ;  (c) 16.0 µC

34. In Fig. 25-28, a potential difference V = 100 V is applied across a capacitor arrangement with capacitances 𝐶1 = 10.0 μF, 𝐶2 = 5.00 μF, and 𝐶3 =  4.00 μF. What are (a) charge q3, (b) potential difference V3, and (c) stored energy U3 for capacitor 3, (d) q1, (e) V1, and (f) U1 for capacitor 1, and (g) q2, (h) V2, and (i) U2 for capacitor 2?

Answer: (a) 400 µC ;  (b) 100 V ;  (c) 20.0 mJ ;  (d) 333 µC ;  (e) 33.3 V ;  (f) 5.56 mJ ;  (g) 333 µC ;  (h) 66.7 V ;  (i) 11.1mJ

50. Figure 25-49 shows a parallel-plate capacitor of plate area A= 10.5 cm2 and plate separation 2d = 7.12 mm. The left half of the gap is filled with material of dielectric constant k1 =  21.0; the top of the right half is filled with material of dielectric constant k2 =  42.0; the bottom of the right half is filled with material of dielectric constant k3 = 58.0.What is the capacitance?

Answer: 4.55×10−11 = 45.5 pF

78. You have many 2.0 μF capacitors, each capable of withstanding 200 V without undergoing electrical breakdown (in which they conduct charge instead of storing it). How would you assemble a combination having an equivalent capacitance of (a) 0.40 μF and (b) 1.2 μF, each combination capable of withstanding 1000 V?

Answer: (a) Five capacitors in series ;  (b) Three arrays of Five capacitors in series connected in parallel